APPENDICE

ROUTINES

Routine di erase

Sintassi:

erasem (wlt,ewlt,eblt,wltrv,healvel,

crdmm,crdms,

eb,row, it,

ret)

Parametri:

| VARIABILI | DEFINIZIONE | VALORE TEST |
| --- | --- | --- |
| wlt | Seleziona la tensione da applicare sulle wordlines per la fase di load. | (0x50 7V) |
| ewlt | Seleziona la tensione da applicare sulle wordlines per la fase di pre-program. | (0xff -10V) |
| eblt | Seleziona la tensione da applicare sulle bitlines per la fase di pre-program. | ( 0x30 6V) |
| wltrv | Seleziona la tensione sulle wordlines per l’operazione di erase verify. | (0x26 4V) |
| healvel | Seleziona la tensione sulla wordline per l’operazione di gate-heal. | (0xff 10V) |
| crdmm | Setta il riferimento laterale di corrente per l’operazione di erase verify in applicazione multilevel. | 0x86 |
| crdms | Setta il riferimento centrale di corrente per l’operazioni di erase verify . | 0xcf |
| eb | Indirizzo erase block. | 0x00 |
| row | Indirizzo settore | 0x00 |
| it | Seleziona alimentazione interna o esterna. | 0 int 1ext |
| ret | Numero di tentativi per cancellare un packet. | - |

Figura1 Descrizione dei parametri.

/********************************************************/

/* Filename:                                                                                           */

/* rexx:/erasem.rexx                                                                              */

/********************************************************/

/* Description:                                                                                       */

/*   Algoritmo di erase                                                                           */

/********************************************************/

wltv=line("set wordline for erase verify....>")

wlt=line("set wltrim for load data....>")

ewlt=line("Set WLtrim for erase prog....>")

eblt=line("Set Ltrim for erase prog....>")

eb=line("select # of eb (0 to 7)....>")

ret=line("number of retries pulse......>")

row=line("Select sector address (0 to 128)....>")

it=line(" 0 internal 1 external supply...>")

crdmm=line("set lateral reference....>")

crdms=line("set central reference....>")

healev=line("set heal level ..........>")

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call comm('0x05',eb)

call comm('0x04',row)

call comm('0x03,0x00')

call wrtreg('0x06,0x09')

call set_pcl

call pgm00(it,row,ewlt,eblt,wlt)

do prov=0 to ret

call erasever(eb,ret,wltv,crdmm,crdms,row )

call currcomp

if ans1>0 then leave

else  call gateheal(healev)

end

exit

/*****************************CURRCOMP************************/

currcomp:

call initchip

call comm('0x05,0x00')

call comm('0x03,0x80')

call wrtreg('0x06,0x03')

call wrtreg('0x0b,0x80')

call wrtreg('0x09,0x00')

call set_pcl

call wrtreg('0x0c,0x81')

call wrtreg('0x0f,0x40')

call wrtreg('0x0e,0x01')

call open('results','dut:reports/'currc".rpt",'w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

do inc=0 to 1  ((17*32)-1)

if inc=0 then do

call move('0x0d')

call write(1,wrtsel)

end

else if inc=(17*32-2) then do

call move('0x0d')

call write(1,wrtself)

end

else

call move('0x0d')

call write(1,wrtsel)

call writeln('results',"packet"inc%32||d2c(9)||"Byte"inc%17"\n")

do i=0 to 7

opt("D"i"drvpmu",0)

ans1=mi(1)

if ans1<0 then return ans1

opt("D"i"drvpmu",1)

call echo("Column Current for IO"i||d2c(9)||"= "ans1"\n")

call writeln('results',"Column Current for I/O "i||d2c(9)||" = "ans1"\n")

end

end

call close('results')

call assign(mux1,ground)

call  wrtreg('0x0e,0x00')

call set_pcl

call comm('0x0f,0x80')

exit

/********************************************************/

/* Filename:                                                                                           */

/* rexx:/pgm00.rexx                                                                              */

/********************************************************/

/* Description:                                                                                       */

/* pre-program  algoritm  for erase    si                                                 */

/********************************************************/

parse arg it row ewlt eblt wlt .

do s=0 to 127

do p=0 to 16

call spghldvm(it,wlt)

call wrtreg('0x10,0xb9')

call comm('0x0a,0xff')

call comm('0x0c,0xa9')

call comm('0x0a,0x00')

call comm('0x0c,0x81')

call  pgm00b(ewlt,eblt,it,wlt)

call move('0x07')

call  write(1,wrt)

end

/* *****************end packet **************************/

call wrtreg('0x03,0x00')

row1=x2d(and(row,'0xff'))+1

call wrtreg('0x04',row1)

end

/*********************** end sectors******************** */

exit

/********************************************************/

/* Filename:                                                                                           */

/* rexx:/pg00b.rexx                                                                                */

/********************************************************/

/* Description:                                                                                        */

/* Algoritmo di  pre-program                                                                 */

/********************************************************/

parse arg ewlt eblt it wlt .

do a=0 to 1

call rmpgldhvm(it)

call spghv(it,ewlt,eblt)

call aplpghv

call comm('0x00,0x00') /*6us*/

call rmpghv

call set_pcl

call rspghv

call spghldvm(it,wlt)

call wrtreg('0x10,0xb9')

call comm('0x0a,0xff')

call comm('0x0c,0x99')

call comm('0x0a,0x00')

call comm('0x0c,0x81')

end

exit

/**************************************************************/

/* Filename:                                                                                                       */

/*spghldvm.rexx                                                                                                */

/**************************************************************/

/* Description:                                                                                                    */

/* Setta la  wl e abilita la pompa di low current                                                 */

/**************************************************************/

parse arg it wlt .

call wrtreg('0x0a',wlt)

if it=0 then do

call wrtreg('0x0b,0x80')

call comm('0x0c,0xa0')

end

else do

call wrtreg('0x0c,0x10')

call set('highv1',5)

call assign('mux3','highv1')

call set('highv1',11)

call wrtreg('0x0c,0x38')

call set('highv2',2)

call assign('mux4','highv2')

call set('highv2',6)

end

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/rmpgldhvm.rexx                                                                                   */

/******************************************************* ******/

/* Description:                                                                                                   */

/*  Disabilita la Hv dalla wl and bl                                                                   */

/**************************************************************/

parse arg it .

if it=0 then

call  wrtreg('0x0b,0x80')

else do

call wrtreg('0x0b,0x10')

call set('highv1','0')

call assign('mux3','cpu')

end

call  comm('0x0c,0x00')

exit

/**************************************************************/

/* Filename:                                                                                                        */

/* rexx:/spghvm.rexx                                                                                          */

/***************************************************************/

/* Description:                                                                                                     */

/* Setta la wl and bl  e abilita 6V externamente  o internamente                        */

/* 1.Wltrim setta le wordline                                                                               */

/* 2.BLtrim setta la bl                                                                                          */

/***************************************************************/

parse arg it wlt .

call wrtreg('0x0a',wlt)

call wrtreg('0x0c,0x30')

call wrtreg('0x0b,0x80')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/aplpghvm.rexx                                                                                      */

/**************************************************************/

/* Description:                                                                                                    */

/*  Applica  Hv alla wl and bl e inizia la programmazione                                */

/***************************************************************/

parse arg it wlt .

call wrtreg('0x0a',wlt)

call  wrtreg('0x0b,0xa0')

call comm('0x00,0x00')

pause(5)

call wrtreg('0x0b,0xe0')

if it=1 then do

call wrtreg('0x0c,0x35')

end

else call wrtreg('0x0c,0x36')

exit

/***************************************************************/

/* Filename:                                                                                                         */

/* rexx:/rspghv.rexx                                                                                             */

/***************************************************************/

/* Description:                                                                                                    */

/*  disadilita il low current pump e setta Vpx to vcc                                          */

/***************************************************************/

parse arg it .

call wrtreg('0x0c,0x20')

call wrtreg('0x0b,0x00')

if it=1 then do

call set(highv2,0)

call assign(mux4,cpu)

end

do i=0 to 1

call comm('0x00,0x00')

end

exit

/********************************************************/

/* Filename:                                                                                           */

/* rexx:/erasever.rexx                                                                            */

/********************************************************/

/* Description:                                                                                       */

/* erase and verify a partire dal settore 00                                             */

/********************************************************/

parse arg eb ret wltv crdmm crdms row .

do ep=0 to ret

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call comm('0x05',eb)

call wrtreg('0x10,0x00') /* float bit lines*/

call wrtreg('0x06,0x01') /* disable wordlines */

call sterase

pause(10) /*100ms*/

call rterase

call comm('0x04,0x03')

call wrtreg('0x06,0x09')

/************    read  *************************/

call setup_read(wltv,crdmm,crdms)

call begin_read(row)

call wrtreg('0x00,0x00') /*2us*/

do p=0 to 16

do b=0 to 32

call read(read19,'0x19','0x19','0x19','0x19','0x19')

call hd('0x19','0x19','0x19','0x19','dut:pats/erase',1)

open('proc1','dut:pats/erase',R)

a=readch('proc1',13)

d1= right(a,2)

loa1=insert('0x',d1)

zeros=x2d(and(loa1,'0xff'))

close('proc1')

if zeros ~=256 then  leave

else

fiu=0

end

/* ************ fine bytes ******/

if zeros ~=256 then leave

else fiu1=0

end

/******** fine packets  ***********/

if zeros = 256 then do

call wrtreg ('0x0b,0x80')

call comm('0x00,0x00')

call wrtreg('0x0f,0x40')

call reset_read

exit

end

call reset_read

if ep=ret then do

line(" bad  sector")

exit

end

end

/* **** fine tentativi  ****/

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/sterase.rexx                                                                                          */

/**************************************************************/

/* Description:                                                                                                    */

/* Setta le wl and bitlines trim and applica la tensione negativa sulla wl          */

/*   and positive  voltage to sorces                                                                     */

/**************************************************************/

call wrtreg('0x0a,0xff')

call wrtreg('0x09,0x80')

call wrtreg('0x0c,0x74')

call wrtreg('0x09,0x82')

call wrtreg('0x09,0xc2')

call set('highv2',6)

call assign(mux4,highv2)

call wrtreg('0x0b,0xa0')

call wrtreg('0x09,0xc6')

call wrtreg('0x0c,0x75')

exit

/*************************************************************/

/*  Filename:                                                                                                    */

/* rexx:/rterase.rexx                                                                                          */

/**************************************************************/

/* Description:                                                                                                    */

/* reset la wl e  bitlines trim e disabilita la tensione  negativa sulla wl             */

/*                                                                                                                         */

/**************************************************************/

call wrtreg('0x0c,0x74')

call set('highv2',0)

call assign(mux4,cpu)

do i=0 to 1

call comm('0x00,0x00')

end                        /*2 us*/

call wrtreg('0x09,0xc2')

call wrtreg('0x0b,0x80')

call wrtreg('0x0b,0x00')

call wrtreg('0x09,0x82')

call load('0x00')

call move('0x00')

call write(1,wrt)

pause(0.1)

call wrtreg('0x09,0x80')

call wrtreg('0x09,0x00')

call wrtreg('0x0c,0x00')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/begin_read.rexx                                                                                    */

/**************************************************************/

/* Description:                                                                                                   */

/*   indirizza il byte  0x00  e applica Vpx sulla wl                                            */

/**************************************************************/

call comm('0x04,0x00')

call comm('0x03,0x00')

call comm('0x09,0x80')

call set_pcl

call wrtreg('0x0f,0x50')

call wrtreg ('0x0b,0xa0')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/reset_read.rexx                                                                                     */

/**************************************************************/

/* Description:                                                                                                   */

/* resetta i  riferimentio di corrente per i sense amplifiers                                */

/**************************************************************/

call wrtreg('0x0b,0x80')

call comm('0x0c,0x00')

do i=0 to 1

call comm('0x00,0x00') /* 1us*/

end

call wrtreg('0x0f,0x00')

call wrtreg('0x08,0x00')

call wrtreg('0x0b,0x00')

exit

/*******************************************************/

/* Filename:                                                                                           */

/* rexx:/gateheal.rexx                                                                            */

/********************************************************/

/* Description:                                                                                        */

/* impulso di programmazione dopo un erase verify                             */

/*********************************************************/

parse arg healev .

call wrtreg('0x06,0x19')

call wrtreg('0x12,0x40')

call wrtreg('0x0a',healev)

if it=0 then do

call wrtreg('0x0b,0x88')

call wrtreg('0x0b,0x0a')

call comm('0x00,0x00')

call comm('0x0c,0x80')

end

else do

call wrtreg('0x0b,0x18')

call set(highv1,4)

call assign(mux3,highv1)

call set(highv1,11)

call wrtreg ('0x0b,0x30')

call comm('0x00,0x00')

call comm('0x0c,0x018')

call assign(mux3,cpu)

call set(highv1,0)

end

call comm('0x0c,0x00')

call comm('0x00,0x00')

exit

ROUTINE DI PROGRAMMAZIONE

Sintassi:

program (wltrim,bltrim,wltrimver,

crdmm,crdms,

eb,row, it,

numtent,step,dur,

pgd1,pgd2)

Parametri:

| VARIABILI | DEFINIZIONE | VALORE TEST |
| --- | --- | --- |
| wltrim | Seleziona la tensione da applicare sulle wordlines per la fase di program. | 0x40 |
| bltrim | Seleziona la tensione da applicare sulle bitlines per la fase di program. | 0x30 |
| wltrimver | Seleziona la tensione sulle wordlines per l’operazione di read. | 0x50 |
| crdmm | Setta il riferimento laterale di corrente per l’operazione di read in applicazione multilevel. | 0x86 |
| crdms | Setta il riferimento centrale di corrente per l’operazioni di read sia in apllicazioni multilevel che single level. | 0xCF |
| eb | Indirizzo erase block. | 0x00 |
| row | Indirizzo settore | 0x00 |
| it | Seleziona alimentazione interna o esterna. | 0 int 1ext |
| numtent | Numero di tentativi per programmare un packet. | - |
| step | Seleziona l’aumento del livello di tesione da applicare sulla wordline. | - |
| dur | Setta la durata dell’impulso di programmazione. | - |
| pgd1 pgd2 | Bits da programmare (0-8). Bits da programmare (9-16). | 0x00 livello 00 0xaa livello 10 0x55 livello 01 0xff livello 11 |

Figura 2  Descrizione dei parametri

/*******************************************************************/

/* Filename:                                                                                                      */

/* rexx:/program.rexx                                                                                       */

/**************************************************************/

/* Description:                                                                                                    */

/* Algoritmo di  program                                                                                   */

/**************************************************************/

/* dichiarazione dei parametri*/

parse arg wltrim bltrim wltrimver crdmm crdms eb row it numtent step dur pgd1  pgd2      .

wltrim=line("Set WLtrim for program....>")

bltrim=line("Set bltrim for program....>")

wltrimver=line("Set wltrim for prog verify......>")

crdmm=line("Set lateral refernce for sense amp....>")

crdms=line("Set central refernce for sense amp....>")

eb=line("select # of eb (0 to 7)....>")

row=line("Select sector address (0 to 128)....>")

it=line(" 0 internal 1 external supply...>")

numtent=line("seleziona il numero di impulsi di program....>")

step=line("Set l'ampiezza dello step fra i vari impulsi di prog....>")

dur=line("durata degli impulsi di program....>")

pgd1=line("load first 8 bits ....>")

pgd2=line("load second 8 bits ....>")

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call wrtreg('0x0a',wltrimver)

call wrtreg('0x0b,0x80')

call comm('0x05',eb)

call comm('0x04',row)

call comm('0x03,0x00')

call wrtreg('0x06,0x09')

call set_pcl

call setup_readm(crdmm,crdms)  /* inserire and */

/**************** packet loop*******************************/

do p=0 to 0  /*16*/

call wrtreg('0x10,0xb9')

call comm('0x0a,0xff')

call comm('0x0c,0x01')

call  begin_readm(it)

do r=0 to numtent

mark=0

/****************************** byte loop ****************/

do b=1 to 1   /*32*/

call move('0x1b')

call write(1,rmow2)

conf1(pgd1,pgd2,b)

call echo("W="w)

if w=0xff  then v=0

else    v=1

mark=mark+v

call load(w)

call move('0x1b')

if b=32 then

call write(1,rmow3)

end

/********************** fine byte **********************/

call set_pcl

call wrtreg('0x0b,0x80')

call comm('0x0c,0x00')

if mark ~=0  then do

a=numtent*step

wltrim=x2d(and(wltrim,'0xff'))+a

call multipg(it,wltrimver,wltrim,bltrim,dur,r)

end

else leave

end

/************** fine numero tentativi di program ***********/

if mark~=0 then do

line("packet "p" cattivo")

call wrtreg('0x0f,0x28')

end

call move('0x07')

call write(1,wrt)

end

/* ************************fine sector ********************/

call wrtreg('0x0c,0x20')

call wrtreg('0x0b,0x80')

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

exit

/***************** CONF1************************************/

conf1:

args pgd1 pgd2 b

/* conversione in formato stringa */

pgdat1=d2c(x2d(and(pgd1,'0xff')))

pgdat2=d2c(x2d(and(pgd2,'0xff')))

/* first pulse*/

call read(rmow,'0x1b','0x1b','0x1b','0x1b')

call hd('0x1b','0x1b','0x1b','0x1b','dut:pats/es1',1)

call open('proc1','dut:pats/es1','R')

ing=readch('proc1',13)

d1= right(ing,2)

loa1=insert('0x',d1)

call echo(loa1)

close('proc1')

/* second pulse*/

call read(rmow1,'0x1b','0x1b','0x1b','0x1b')  /*rmow1*/

call hd('0x1b','0x1b','0x1b','0x1b','dut:pats/es2',1)

open('proc2','dut:pats/es2','R')

ing=readch('proc2',13)

d2= right(ing,2)

loa2=insert('0x',d2)

call echo(loa2)

close('proc2')

patt1=and(loa1,'0xff')

a1=x2d(patt1)

pat1=d2c(a1)

patt2=and(loa2,'0xff')

a2=x2d(patt2)

pat2=d2c(a2)

/* xor */

modify1.1=bitxor(pat1,pgdat1)

modify1.2=bitxor(pat2, pgdat2)

do i=1 to 2

a0.i=bittst(modify1.i,0)

a1.i=bittst(modify1.i,1)

a2.i=bittst(modify1.i,2)

a3.i=bittst(modify1.i,3)

a4.i=bittst(modify1.i,4)

a5.i=bittst(modify1.i,5)

a6.i=bittst(modify1.i,6)

a7.i=bittst(modify1.i,7)

if (a0.i=0 & a1.i=0) then b1.i=1

else  b1.i=0

if (a2.i=0 & a3.i=0) then b2.i=1

else  b2.i=0

dat1.i=insert(b2.i,b1.i)

if (a4.i=0 & a5.i=0) then b3.i=1

else  b3.i=0

dat2.i=insert(b3.i,dat1.i)

if (a6.i=0 & a7.i=0) then b4.i=1

else  b4.i=0

word1.i=insert(b4.i,dat2.i)

end

w1=b1.1*1+b2.1*2+b3.1*4+b4.1*8

w2=b1.2*16+b2.2*32+b3.2*64+b4.2*128

word=(insert(word1.2,word1.1))

w=w1+w2

return  w

/*************************************************************/

/* Filename:                                                                                                    */

/* rexx:/setup_readm.rexx                                                                               */

/*************************************************************/

/* Description:                                                                                                 */

/* setta i riferimenti laterali e  quello   centrale                                             */

/************************************************************/

parse arg crdmm crdms .

call wrtreg('0x0f,0x28')

call wrtreg('0x07',crdmm)

call comm('0x08',crdms)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/begin_readm.rexx                                                                                */

/**************************************************************/

/* Description:                                                                                                   */

/* carica il  byte di indirizzo 00  e abilita la pompa di low current                */

/*************************************************************/

parse arg it .

call comm('0x09,0x80') /*00 anzichè 80 for no auto increment*/

if it=0 then

call wrtreg ('0x0b,0xa0')

else do

call wrtreg('0x0b,0x3c')

call set(highv1,5)

call assign(mux3,highv1)

call set(highv1,11)

end

exit

/*************************************************************/

/* Filename                                                                                                        */

/* rexx:/multipg.rexx                                                                                         */

/*************************************************************/

/* Description:                                                                                                   */

/*  algoritmo per la  fase di programmazione                                                  */

/*************************************************************/

parse arg it wltrimver wltrim bltrim dur r .

call wrtreg('0x0f,0x00')

call spghvm(it,wltrim,bltrim)

call aplpghvm(it,dur,r)

call rmpghvm(it)

call set_pcl

call wrtreg('0x0a',wltrimver)

call wrtreg('0x0b,0x80')

call wrtreg('0x0f,0x28')

exit

/***********************************************************/

/* Filename:                                                                                                  */

/* rexx:/spghvm.rexx                                                                                    */

/********************************************************** */

/* Description:                                                                                               */

/* Setta le wl e bl, abilita  low current pump 6V esterni o interna                */

/* 1.Wltrim setta the wordline per il program                                                */

/* 2.BLtrim set the bl, valore   raccomandato  30h                                         */

/*************************************************************/

parse arg it wlt blt .

call wrtreg('0x0a',wlt)

call wrtreg('0x0c',blt)

if it=1 then do

call assign(mux4,highv2)

call set(highv2,6)

call wrtreg('0x0c,0x31')

end

else

call wrtreg('0x0c,0x32')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/aplpghvm.rexx                                                 			            */

/**************************************************************/

/* Description:                                                                                                   */

/*  applica  Hv alla wl e bl  selezionate e inizia la programmazione                */

/**************************************************************/

parse arg it durata r .

call  wrtreg('0x0b,0x80')

call comm('0x0c,0xc0')

call comm('0x0c,0xe0')

if (it)=1 then

call wrtreg('0x0c,0x35')

else call wrtreg('0x0c,0x36')

time=(durata-r)

do  d=0 to time

call comm('0x00,0x00')

end

exit

/**************************************************************/

/* Filename:                                                                                                        */

/* rexx:/rspghvm.rexx                                                                                         */

/**************************************************************/

/* Description:                                                                                                    */

/*  disabilita low current pump  e setta Vpx a vcc                                           */

/**************************************************************/

call comm('0x0c,0x31')

call  wrtreg('0x0b,0xc0')

call comm('0x0c,0x80')

call comm('0x0c,0x00')

if it=1 then do

call set(highv2,0)

call assign(mux4,cpu)

end

/*************************************************************/

/* Filename:                                                                                                     */

/*   rexx_common:init.rexx                                                                              */

/*************************************************************/

/* Description:                                                                                                  */

/*    file di inizializzazione per M01 Flash Memory                                        */

/**************************************************************/

address command 'assign rexx: tester:duts/flash/m01/rexx'

call settype

call text("text","off")

whatsys = getclip('hpltype')

numdats=getvar('dut.numiobits')

numrows=getvar('dut.numrows')

numcols=getvar('dut.numcolumns')

partsize = numrows * numcols % 1048576

if whatsys = '2001' then call loadsys('dut:macs/prova1')

else call loadsys('dut:macs/dutvl1')

call loadepe('dut:epe/dut')

call clkcal('dut:cal/clock')

call skewcal('dut:cal/skew')

call assign('mux1','cpu')

if numdats = 16 then call assign('mux2','cpu')

else call assign('mux2','ground')

call assign('mux3','cpu')

call assign('mux4','cpu')

call assign('mux5','cpu')

call assign('mux6','cpu')

call assign('mux7','cpu')

if partsize = 8 then call assign('mux8','in2')

call assign('mux8','cpu')

call set('ivcc1','200')

call 'loadepecross-cpu'

call mi('0')

call write('1','init')

call text("text","on")

call supply('vcc1')

call echo("low voltage command mode macros loaded\n")

exit

/*********************** flash Continuity Test*************** */

/*trace results*/

Signal on Syntax

signal on halt

type=getclip('hpltype')

/*variables defined */

numadds=23

numdats=8

numclks=5

maxpass=-0.2

minpass=-1.8

fc=-0.0001			/*  corrente da forzare */

Call echo("\nPerforming Continuity Test\n\n")

call echo("\nConditions force I= " fc "\n")

call echo("\nfail is above" maxpass "v or below " minpass "v\n")

Cond = Pass

/* Power Down */

Call vcc("0.50")

/* Test Clock Pins */

Do i = 1 to NumClks

opt("C"i"pmucnct", 0)

opt("C"i"discnct", 1)

Volt = mv(fc)

If DataType(Volt) ~= "NUM" Then Do

call echo("\nPMU Error During Continuity Test\n")

Address command 'rx' 'df0:mtrx' 'Recall' NumClks NumAdds NumDats

Exit

End /* if */

If (Volt > maxpass | Volt < minpass) Then

Do

cond = Fail

call echo("	Clock "i" not connected"  Volt  "\n")

End

opt("C"i"pmucnct", 1)

opt("C"i"discnct", 0)

End i

/* Test Data Pins */

Do i = 0 to NumDats-1

opt("D"i"drvpmu", 0)

opt("D"i"rcvpmu", 0)

Volt = mv(fc)

If DataType(Volt) ~= "NUM" Then Do

Call echo("\nPMU Error During Continuity Test\n")

Address command 'rx' 'df0:mtrx' 'Recall' NumClks NumAdds NumDats

Exit

End /* if */

If (Volt > maxpass | Volt < minpass) Then

Do

cond = Fail

call echo("	Data "i" not connected"  Volt  "\n")

end

else call echo("data "i"pass""\n" )

opt("D"i"drvpmu", 1)

opt("D"i"rcvpmu", 1)

End i

/* Test Address Pins */

do i=0 to NumAdds-1

opt("A"i"pmu", 0)

opt("A"i"discnct", 1)

Volt = mv(fc)

If DataType(Volt) ~= "NUM" Then Do

Call echo("\nPMU Error During Continuity Test\n" )

Address command 'rx' 'df0:mtrx' 'Recall' NumClks NumAdds NumDats

Exit

End /* if */

If (Volt > maxpass | Volt < minpass) Then

Do

cond = Fail

call echo("	Address "i" not connected"  Volt  "\n")

End

else call echo("pass address"i"\n ")

opt("A"i"pmu", 1)

opt("A"i"discnct", 0)

End i

end

Syntax:

halt:

/* Restore old EPE */

call vcc("3.3")

/* Report Results */

Call echo("\nContinuity Result = "cond"\n")

setclip("TesRes", cond)

Call text("text", "on")

Exit

/**********************************************/

/* Filename:                                                                      */

/* rexx:/wrtreg.rexx                                                          */

/**********************************************/

/* Description:                                                                   */

/* carica dati nei registri                                                    */

/**********************************************/

parse arg addreg data .

call move('0x0b')

call load(addreg)

call write(1,wrt)

call move('0x0c')

call load(data)

call write(1,wrt)

exit

/********************************************/

/* Filename:                                                                   */

/* rexx:/initchip.rexx                                                     */

/********************************************/

/* Description:                                                               */

/* resetta tutti i registri e abilita la  Vref                        */

/********************************************/

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

call wrtreg('0x0d,0x10')

exit

/*p abilita il chip*/

call move('0x08')

call load('0x00')

call write(1,select_chip)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/set_pcl.rexx                                                                                           */

/*************************************************************/

/* Description:                                                                                                   */

/* scarica tutte le bitlines  disabilita  colfloat_                                                */

/*************************************************************/

call wrtreg('0x10,0x03')

call wrtreg('0x10,0x01')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/check.rexx                                                                                            */

/**************************************************************/

/* Description:                                                                                                   */

/* verifica la funzionalita dei registri di indirizzamento                                  */

/*************************************************************/

call p

call move('0x02')

call load('0x80')

call write(1,select_chip)

call move('0x0f')

call load('0x10')

call write(1,select_chip)

do i=0 to 16

call comm('0x0b,0x01')

call read(read1A,'0x1a','0x1a','0x1a','0x1a')

call hd('0x1a','0x1a','0x1a','0x1a','dut:pats/pack',1)

call open('pac','dut:pats/pack','R')

ing=readch('pac',13)

d1= right(ing,2)

loa=insert('0x',d1)

close('pac')

if i=0 then do

call open('results','dut:reports/prova.rpt','w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

end

call writeln('results',"packet = "loa)

call comm('0x0d,0x00')

end

call close('results')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/check reg.rexx                                                                                      */

/**************************************************************/

/* Description:                                                                                                   */

/* verifica la funzionalita' dei registri                                                               */

/**************************************************************/

call p

call move('0x02')

call load('0x80')

call write(1,select_chip)

call open('results','dut:reports/prova.rpt','w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

call comm('0x09,0xff')

call comm('0x0b,0x01')

call read(read1A,'0x1a','0x1a','0x1a','0x1a')

call hd('0x1a','0x1a','0x1a','0x1a','dut:pats/pack',1)

call open('pac','dut:pats/pack','R')

ing=readch('pac',13)

d1= right(ing,2)

loa=insert('0x',d1)

close('pac')

call writeln('results'," = "loa)

call comm('0x09,0x55')

call comm('0x0b,0x01')

call read(read1A,'0x1a','0x1a','0x1a','0x1a')

call hd('0x1a','0x1a','0x1a','0x1a','dut:pats/pack',1)

call open('pac','dut:pats/pack','R')

ing=readch('pac',13)

d1= right(ing,2)

loa=insert('0x',d1)

close('pac')

call writeln('results'," = "loa)

call comm('0x0b,0x08')

call read(read1A,'0x1a','0x1a','0x1a','0x1a')

call hd('0x1a','0x1a','0x1a','0x1a','dut:pats/pack',1)

call open('pac','dut:pats/pack','R')

ing=readch('pac',13)

d1= right(ing,2)

loa=insert('0x',d1)

close('pac')

call writeln('results'," = "loa)

close('results')

call comm('0x0f,0x08')

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/hvcon.rexx                                                                                             */

/**************************************************************/

/* Description:                                                                                                    */

/* confronta la tensione sulla wordline con una di riferimento applicata sui     */

/*  pads. Quando il segnale di sel_out si porta al livello basso la tensione       */

/*     di riferimento coincide con quella all'uscita della pompa.                        */

/**************************************************************/

call p

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call wrtreg('0x12,0x00')

call wrtreg('0x0a,0x80')

call wrtreg('0x0b,0x10')

call wrtreg('0x0b,0x80')

call wrtreg('0x0e,0x02')

call wrtreg('0x0b,0xa0')

call wrtreg('0x0b,0x30')

a=line("change")

call load('0x01')

call write(1,wrtself)

call comm('0x0c,0x00')

call comm('0x0e,0x00')

call comm('0x0f,0x08')

exit

/********************************************/

/* Filename:                                                                   */

/* rexx:/refcel.rexx                                                         */

/********************************************/

/* Description:                                                                */

/* legge la tensione di riferimento Vref                         */

/****************************************** */

call move('0x02')

call load('0x80')

call write(1,select_chip)

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

call wrtreg('0x0d,0x18')

pause(1)

call comm('0x0b,0x0f')

call move('0x0c')

call load('0x10')

call write(1,padl)

opt("D1drvpmu",0)

ans1=pmv()

opt("D1drvpmu",1)

call wrtreg('0x0d,0x00')

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/****************************************************************/

/* Filename:                                                                                                           */

/* rexx:/pfcel.rexx                                                                                                  */

/***************************************************************/

/* Description:                                                                                                      */

/*programma la cella flash che fornisce la tensione di riferimento Vref             */

/***************************************************************/

call move('0x02')

call load('0x80')

call write(1,select_chip)

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

call wrtreg('0x0d,0x0c')

call comm('0x09,0x00')

spghv('1','0xff')

aplpghv('1','0xff')

pause(1)

rmpghv('1')

rspghv('1')

call wrtreg('0x0d,0x10')

call wrtreg('0x0d,0x00')

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/efcel.rexx                                                                                               */

/**************************************************************/

/* Description:                                                                                                    */

/*     cancella la cella adibita a fornire la tensione Vref                                     */

/**************************************************************/

call move('0x02')

call load('0x80')

call write(1,select_chip)

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

call wrtreg('0x0d,0x0c')

pause(1)

sterase

pause(10)

rterase

call wrtreg('0x0d,0x10')

call wrtreg('0x0d,0x00')

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/idsref.rexx                                                                                             */

/***************************************************************/

/*  Description:                                                                                                    */

/*  Routine che effettua la lettura delle correnti di riferimento                           */

/****************************************************************/

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call wrtreg('0x07,0x86')

call wrtreg('0x08,0x9f')

call wrtreg('0x0f,0x08')

call wrtreg('0x0b,0x80')

call comm('0x0b,0x0e')

call move('0x0c')

call load('0x01')

call write(1,padl)

call open('results','dut:reports/ref.rpt','w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

opt("D"0"drvpmu",0)

ans0=mi(1)

pause(1)

opt("D"1"drvpmu",0)

ans1=mi(1)

pause(1)

opt("D2drvpmu",0)

ans2=mi(1)

opt("D"2"drvpmu",1)

opt("D"1"drvpmu",1)

opt("D"0"drvpmu",1)

call writeln('results',"Column Current for I/O "i||d2c(9)||" = "anso ans1 ans2"\n")

call close('results')

call wrtreg('0x0e,0x00')

call wrtreg('0x0b,0x00')

pause(1)

call wrtreg('0x08,0x00')

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/ersaref.rexx                                                                                           */

/***************************************************************/

/* Description:                                                                                                   */

/* cancella le celle adibite a fornire la corrente di riferimento                         */

/* per i sense amplifiers                                                                                    */

/***************************************************************/

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call wrtreg('0x08,0x10')

call sterase

pause(10)

call rterase

call wrtreg('0x08,0x80')

call wrtreg('0x0f,0x08')

pause(1)

call wrtreg('0x08,0x00')

call wrtreg('0x0b,0x08')

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/***************************************************************/

/* Filename:                                                                                                       */

/* rexx:/pgsaref.rexx                                                                                          */

/***************************************************************/

/* Description:                                                                                                    */

/* programma le celle di riferimento dei sense amp                                        */

/**************************************************************/

it=line('it')

wlt=line('wlt')

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call wrtreg('0x08,0x90')

call wrtreg('0x0f,0x08')

call wrtreg('0x12,0x03')

call spghv('1','0x30')

call aplpghv('1','0x30')

pause(5)

call rmpghv('1')

call rspghv('1')

call wrtreg('0x08,0x10')

call comm('0x00,0x00')

call wrtreg('0x08,0x00')

end

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/***************************************************************/

/* Filename:                                                                                                       */

/* rexx:/vsref.rexx                                                                                              */

/**************************************************************/

/* Description:                                                                                                    */

/* misura la tensione Vd delle celle di riferimento                                           */

/***************************************************************/

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call wrtreg('0x07,0xf0')

call wrtreg('0x08,0x93')

call wrtreg('0x0f,0x08')

call wrtreg('0x0b,0x88')

call wrtreg('0x0f,0x10')

call comm('0x0b,0x0e')

call move('0x0c')

call load('0x01')

call write(1,padl)

call open('results','dut:reports/ref.rpt','w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

opt("D0drvpmu",0)

ans1=mv(0.000001)

opt("D"0"drvpmu",1)

call writeln('results',"Column Current for I/O "i||d2c(9)||" = "ans1"\n")

call close('results')

call wrtreg('0x0e,0x00')

call wrtreg('0x0b,0x08')

call comm('0x00,0x00')

call wrtreg('0x08,0x00')

call wrtreg('0x0f,0x00')

call wrtreg('0x0b,0x00')

call move('0x0f')

call load('0x08')

call write(1,wrtsel)

exit

/* Rexx: vcc.rexx**************************************/

/******** vcc - Setta  VCC1 a 3.3V******************** */

parse arg vc1

if (vc1 = "") then do

call set("vcc1",3.3)

call echo("Vcc1 set to 5v default \n")

exit

end

if ((vc1 = ?) |(vc1 < 0) |(vc1 > 7)) then do

call echo("Usage: vcc(volts) \n")

call echo("volts  - VCC value in Volts \n")

call echo(" Acceptable Range: 0 - 7 Volts \n")

exit

end

call set("vcc1",vc1)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/ids_read.rexx                                                                                        */

/**************************************************************/

/* Description:                                                                                                    */

/* misura la corrente delle celle selezionate con l'opzione di variare                */

/* la tensione di gate con il parametro wltrim                                                   */

/**************************************************************/

parse arg wltrim .

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call comm('0x05,0x03')

call comm('0x04,0x03')

call comm('0x03,0x0b')

call wrtreg('0x06,0x09')

call wrtreg('0x0a',wltrim)

call wrtreg('0x0b,0x80')

call comm('0x09,0x00')

call set_pcl

call wrtreg('0x0f,0x40')

call wrtreg('0x0a',wltrim)

call wrtreg('0x0b,0xa0')

do i=0 to 1

call comm('0x00,0x00')

end

call comm('0x0b,0x0e')

call move('0x0c')

call load('0x01')

call write(1,padl)

call open('results','dut:reports/wlt.rpt','w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

do inc=0 to 1

if inc=1 then do

call move('0x0d')

call write(1,wrtsel)

end

else do

call move('0x0d')

call write(1,wrtsel)

end

call writeln('results',"Byte"inc"\n")

do i=0 to 7

opt("D"i"drvpmu",0)

ans1=mi(1)

opt("D"i"drvpmu",1)

call writeln('results',"Column Current for I/O "i||d2c(9)||" = "ans1"\n")

end

end

call close('results')

call wrtreg('0x0b,0x80')

call  wrtreg('0x0e,0x00')

call wrtreg('0x10,0x03')

call wrtreg('0x10,0x00')

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

exit

/**************************************************************/

/* Filename:                                                                                                       */

/* rexx:/vdid.rexx                                                                                               */

/**************************************************************/

/* Description:                                                                                                    */

/* routine che implementa un algoritmo per misurare la corrente di drain        */

/* al variare della tensione sul gate                                                                    */

/**************************************************************/

parse arg wltrim .

call open('results','dut:reports/vdid.rpt','w')

call writeln('results',"***** Report File on Column Current *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

call writeln('results',"VD ID ")

call writeln('results'," ")

do r=1 to 15

a=r*0.5

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call comm('0x05,0x03')

call comm('0x04,0x04')

call comm('0x03,0x02')

call wrtreg('0x06,0x09')

call wrtreg('0x0b,0x80')

call wrtreg('0x0f,0x40')

call set_pcl

call comm('0x09,0x00')

call wrtreg('0x0a',wltrim)

call wrtreg('0x0b,0xa0')

do i=0 to 1

call comm('0x00,0x00')

end

call comm('0x0b,0x0e')

call move('0x0c')

call load('0x01')

call write(1,padl)

call move('0x0d')

call write(1,wrtsel)

opt("D"0"drvpmu",0)

ans1=mi(a)

opt("D"0"drvpmu",1)

call writeln('results', a   ans1"\n")

call wrtreg('0x0b,0x80')

call  wrtreg('0x0e,0x00')

call wrtreg('0x10,0x03')

call wrtreg('0x10,0x00')

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

pause(2)

end

call close('results')

exit

/*****************************************************/

/* Filename:                                                                                     */

/* rexx:/statistic.rexx                                                                        */

/*****************************************************/

/* Description:                                                                                  */

/*    programma un 1Kb di memoria e misura la corrente di drain  */

/*    ad ogni impulso di programmazione                                         */

/*****************************************************/

it=line('scegli alimentazione interna 0 o esterna 1…………>')

finestep=line('scegli il numero di impulsi diprogrammazione……>')

amp=line(' scegli lo step di tensione tra un impulso e il successivo…>')

eb=line('seleziona l'erase block……………..>')

sct=line('seleziona il settore……………..>')

pac=line('seleziona il pacchetto……………..>')

call open('results','dut:reports/algo.rpt','w')

call writeln('results',"***** Report File on Column Current  *****")

call writeln('results'," ")

call writeln('results',"Date : "date() ||d2c(9)|| "Time : "time())

call writeln('results'," ")

do c=0 to finestep

wlt=16+amp*c

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call comm('0x05',eb)

call comm('0x04',sct)

call comm('0x03',pac)

call wrtreg('0x06,0x09')

call wrtreg('0x0a,0x50')

call wrtreg('0x0b,0x80')

call comm('0x09,0x00')

call set_pcl

call wrtreg('0x0f,0x40')

call wrtreg('0x0a,0x50')

call wrtreg('0x0b,0xa0')

do t=0 to 1

call comm('0x00,0x00')

end

call comm('0x0b,0x0e')

call move('0x0c')

call load('0x01')

call write(1,padl)

do p=0 to 5

do inc=0 to  31

call move('0x0d')

call write(1,wrtsel)

call writeln('results',"Byte"inc"\n")

do i=0 to 7

opt("D"i"drvpmu",0)

ans1=mi(1)

opt("D"i"drvpmu",1)

call writeln('results',"            "ans1"\n")

end inc

end p

call wrtreg('0x0b,0x80')

call  wrtreg('0x0e,0x00')

call wrtreg('0x10,0x03')

call wrtreg('0x10,0x00')

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

pause(8)

call move('0x02')

call load('0x80')

call write(1,select_chip)

call initchip

call comm('0x05,eb)

call comm('0x04',sct)

call comm('0x03',pac)

call wrtreg('0x06,0x09')

call spghv(it,wlt)

call comm('0x09,0x80')

call wrtreg('0x10,0x81')

do p1=0 to  5

do b1=0 to 31

call move('0x0a')

call load('0x00')

call write(1,ra)

end

call aplpghv(it,wlt)

pause(1)

call rmpghv(it)

if p1=5 leave

else

call comm('0x07,0x00')

end p1

call rspghv(it)

call wrtreg('0x06,0x0b')

call wrtreg('0x06,0x09')

call move('0x0f')

call load('0x18')

call write(1,wrtsel)

call writeln('results',"***********program************" wlt"\n")

end

call close('results')

exit