## Slide 1: Conductors and Insulators
By now you should be well aware of the correlation between electrical conductivity and certain types of materials. Those materials allowing for easy passage of free electrons are called conductors, while those materials impeding the passage of free electrons are called insulators.

## Slide 2: Conductors
Metal atoms have outer electrons which are not tied to any atom. These electrons can move freely within the structure of a metal.
When more electrons are pushed into a piece of metal (by an electric current for example) the electrons just flow through the metal in between the metal atoms.
The electric current flowing through the wire is a flow of electrons.

## Slide 3: CONDUCTORS
These are materials in which it is easy to get electrons to move and provide a flow of electric current.
Conductors are mostly metals such as gold, silver, copper, iron and lead.
Carbon is a conductor as well as some gases (as in fluorescent tubes) and water containing some chemicals.
  These are not perfect conductors and offer some resistance to the flow of current.

## Slide 4: Resistance of a conductor
The resistance of a conductor (such as a metal rod) is determined by three things:
Its length. The longer its length the higher its resistance.
Its cross-sectional area. The bigger this is the lower is its resistance.
the material of which it is made. All materials have RESISTIVITY. The higher the value of resistivity the higher the resistance. It is measured in OHM METERS.
length x resistivity Resistance = ------------------------------- cross-sectional area

## Slide 5
Ball bearings rolling through a forest of nails model electron motion in a conductor. (Disc 17-22, 41 sec.)

## Slide 6: INSULATORS
These are materials in which it is difficult to get current to flow. Examples are rubber, pvc, paper, polystyrene and oil. Even with these it is possible to get some current flowing if the applied voltage is high enough.

## Slide 7: Semiconductors
There is another class of materials called semi-conductors.
These have a resistance between insulators and conductors.
Examples are silicon and germanium and are used in diodes and transistors.

## Slide 8: Band gap
Semiconductors are very similar to insulators. The two categories of solids differ primarily in that insulators have larger band gaps — energies that electrons must acquire to be free to flow.

## Slide 9
In semiconductors at room temperature, just as in insulators, very few electrons gain enough thermal energy to leap the band gap, which is necessary for conduction.

## Slide 10
For this reason, pure semiconductors and insulators, in the absence of applied fields, have roughly similar electrical properties. The smaller bandgaps of semiconductors, however, allow for many other means besides temperature to control their electrical properties.

## Slide 11
When metal atoms interact together to form a solid, their atomic orbitals mix to form a continuous band of orbitals. In the representation of 1 Na atom (left-hand side of diagram), the blue dot represents an electron in the 3s orbital.

## Slide 12
In the representation of many Na atoms (center of diagram), the blue dots again represent electrons in the "mixed" orbitals that are formed when many atoms interact.
This "mixing" of orbitals is better represented by a "band" of orbitals (right-hand side of diagram), in which the blue area represents orbitals that are filled with electrons.

## Slide 13
When nonmetal atoms interact to form a solid, their atomic orbitals mix to form two bands of orbitals, separated by a large band gap.
When semimetal atoms interact to form a solid, their atomic orbitals mix to form two bands of orbitals, separated by a small band gap.

## Slide 14: Silicon and Germanium
Solid state electronics arises from the unique properties of silicon and germanium, each of which has four valence electrons and which form crystal lattices in which substituted atoms (dopants) can dramatically change the electrical properties.

## Slide 15: Silicon
In solid state electronics, either pure silicon or germanium may be used as the intrinsic semiconductor which forms the starting point for fabrication. Each has four valence electrons, even if germanium will at a given temperature have more free electrons and a higher conductivity.
Silicon is by far the most widely used semiconductor for electronics, partly because it can be used at much higher temperatures than germanium.
valence electrons

## Slide 16: Germanium
Germanium will at a given temperature have more free electrons and a higher conductivity
The electrons in the outermost shell of an atom are called valence electrons

## Slide 17: Intrinsic Semiconductor
Valence Electrons: the electrons in the outermost shell of an atom are called valence electrons.
Schematic diagram showing only the valence electron shell to illustrate intrinsic, semiconductors.
It is difficult to get current to flow because there is no free electron
The electrical properties of matter are pictured in the band theory of solids in terms of how much energy it takes to free a valence electron.

## Slide 18: Intrinsic Semiconductor
A silicon crystal is different from an insulator because at any temperature above absolute zero temperature, there is a finite probability that an electron in the lattice will be knocked loose from its position, leaving behind an electron deficiency called a "hole".
If a voltage is applied, then both the electron and the hole can contribute to a small current flow.

## Slide 19: Semiconductor Current
The current which will flow in an intrinsic semiconductor consists of both electron and hole current. That is, the electrons which have been freed from their lattice positions into the conduction band can move through the material.

## Slide 20
In addition, other electrons can hop between lattice positions to fill the vacancies left by the freed electrons. This additional mechanism is called hole conduction because it is as if the holes are migrating across the material in the direction opposite to the free electron movement.
N.B.:
Both currents are very low ones
(10÷20 nA)

## Slide 21: The Doping of Semiconductors
The addition of a small percentage of foreign atoms in the regular crystal lattice of silicon or germanium produces dramatic changes in their electrical properties, producing n-type and p-type semiconductors.
Pentavalent impurities: Impurity atoms with 5 valence electrons produce n-type semiconductors by contributing extra electrons.
Trivalent impurities: Impurity atoms with 3 valence electrons produce p-type semiconductors by producing a "hole" or electron deficiency.

## Slide 22: Impurity atoms
Pentavalent
Trivalent

## Slide 23: N-Type Semiconductor
The addition of pentavalent impurities such as antimony, arsenic or phosphorous contributes free electrons, greatly increasing the conductivity of the intrinsic semiconductor
Schematic diagrams showing only the valence electron shell to illustrate n-type semiconductors.

## Slide 24: P-Type Semiconductor
The addition of trivalent impurities such as boron, aluminum or gallium to an intrinsic semiconductor creates deficiencies of valence electrons,called "holes".

## Slide 25: P-N Junction
When p-type and n-type materials are placed in contact with each other, the junction behaves very differently than either type of material alone.
Specifically, current will flow readily in one direction (forward biased) but not in the other (reverse biased), creating the basic diode.
This non-reversing behavior arises from the nature of the charge transport process in the two types of materials.

## Slide 26: Depletion Region
When a p-n junction is formed, some of the free electrons in the n-region diffuse across the junction and combine with holes to form negative ions. In so doing they leave behind positive ions at the donor impurity sites.

## Slide 27
Depletion Region Details
In the p-type region there are holes from the acceptor impurities and in the n-type region there are extra electrons
When a p-n junction is formed some of the electrons from the n-region
which have reached the conduction band are free to diffuse across the junction and combine with holes.

## Slide 28
Depletion Region Details
Filling a hole makes a negative ion and leaves behind a positive ion on the n-side. A space charge builds up, creating a depletion region which inhibits any further electron transfer unless it is helped by putting a forward bias on the junction.

## Slide 29
Forward Biased P-N Junction
When an external battery is connected across a p–n junction, the amount of current flow is determined by the polarity of the applied voltage and its effect on the space–charge region.
the positive terminal of the external battery is connected to the p–type material and the negative terminal to the n–type material.

## Slide 30
Electrons can then proceed further leftward by jumping from hole to hole, so the holes can be said to be moving to the right in this process.
The forward current in a p-n junction when it is forward-biased (illustrated below) involves electrons from the n-type material moving leftward across the junction and combining with holes in the p-type material.

## Slide 31
Excess electrons from the n–type material can then penetrate the space charge region, flow across the junction, and move by way of the holes in the p–type material toward the positive terminal of the battery. This electron flow continues as long as the external voltage is applied. Under these conditions, the junction is said to be forward–biased.

## Slide 32
In this arrangement, electrons in the p–type material near the positive terminal of the battery break their electron–pair bonds and enter the battery, creating new holes. At the same time, electrons from the negative terminal of the battery enter the n–type material and diffuse toward the junction.

## Slide 33
Reverse Biased P-N Junction
The positive terminal of the battery is connected to the n–type material and the negative terminal to the p–type material.
In this arrangement, the free electrons in the n–type material are attracted toward the positive terminal of the battery and away from the junction.
At the same time, holes from the p–type material are attracted toward, the negative terminal of the battery and away from the junction.

## Slide 34
As a result, the depletion region at the junction becomes effectively wider.
A transient current flows as both electrons and holes are pulled away from the junction. When the potential formed by the widened depletion layer equals the applied voltage, the current will cease except for the small thermal current.
Reverse Biased P-N Junction

## Slide 35: Reverse Biased P-N Junction
The application of a reverse voltage to the p-n junction will cause a transient current to flow as both electrons and holes are pulled away from the junction. When the potential formed by the widened depletion layer equals the applied voltage, the current will cease except for the small thermal current.

## Slide 36: Forward Biased P-N Junction
Forward biasing the p-n junction drives holes to the junction from the p-type material and electrons to the junction from the n-type material. At the junction the electrons and holes combine so that a continuous current can be maintained.

## Slide 37
WHAT IS A DIODE?
A DIODE IS AN ELECTRONIC DEVICE HAVING
TWO ELECTRODES (OR TERMINALS)
A CATHODE AND AN ANODE

## Slide 38
Semiconductor diode markings

## Slide 39
Voltage–current characteristic
The voltage–current characteristic for a p–n junction shows both the reverse–bias and forward–bias regions

## Slide 40
In the forward–bias region, current rises rapidly as the voltage is increased and is quite high. Current in the reverse–bias region is usually much lower. Excessive voltage ( bias ) in either direction should be avoided in normal applications because excessive currents and the resulting high temperatures may permanently damage the semiconductor device.