Tutte le connessioni  microfoniche esistenti

POPULAR MICROPHONE PLUG AND SOCKET PINOUTS.

X=(cannon x) L=(Latch) R=(rubber compound)

SKIP TO

# TRIO/KENWOOD.

## KENWOOD MICROPHONES.

KENWOOD- MC-10 MICROPHONE. 
KENWOOD- MC-30 / 35 MICROPHONE.
KENWOOD- MC-42S MICROPHONE. 
KENWOOD- MC-43 MICROPHONE. 
KENWOOD- MC-44 MICROPHONE. 
KENWOOD- MC-45 MICROPHONE (mk1). 
KENWOOD- MC-45 MICROPHONE (mk2).
KENWOOD- MC-46 MICROPHONE. 
KENWOOD- MC-47 MICROPHONE. 
KENWOOD- MC-48B MICROPHONE. 
KENWOOD- MC-50 MICROPHONE. pdf. 
KENWOOD- MC-52DM MICROPHONE. 
KENWOOD- MC-53DM MICROPHONE.
KENWOOD- MC-55 MICROPHONE.
KENWOOD- MC-57 MICROPHONE. 
KENWOOD- MC-58 MICROPHONE. 
KENWOOD- MC-59 MICROPHONE.
KENWOOD- MC-60 MICROPHONE. 
KENWOOD- MC-60A MICROPHONE. 
KENWOOD- MC-80 MICROPHONE.
KENWOOD- MC-85 MICROPHONE. 
KENWOOD- MC-85 SCHEMATIC pdf. 
KENWOOD- MC-90 MICROPHONE.
KENWOOD- SMC-25 SMC-30 SPEAKER/MIC. 
KENWOOD- SMC-32 SPEAKER/MIC. 
KENWOOD- SMC-33 SPEAKER/MIC.
KENWOOD- SMC-32 SMC-33 SMC-34 SCHEMATIC pdf.
KENWOOD- KMC-9C KMC-30 KMC-32 KMC-35 KMC-36 MICROPHONES.

### MJ-88 CONNECTING CABLE.

KENWOOD MICROPHONE COMPATIBILITY LIST pdf.

### MORE KENWOOD CONNECTION INFO.pdf file

### KENWOOD INSTRUCTION MANUAL & CONTROL SOFTWARE.

KENWOOD( Handheld Tranceiver's )-TH-22A/AE TH-28/AE TH-42A/AE TH-48/AE TH-78A/E TH-F6 TH-F7 TH-F7E THG-71 TH-D7A/E
TH-K2AT TH-K2E TH-K4E TH-K4AT TH-235 UBZ-LJ8BE UBZ-LJ8SLE UBZ-LJ8YE VBZ-LH14 VBZ-LF AR-14 GR-14 
( see SMC-32 SMC-33 SMC-34 above for external microphone and PC interconnection )

KENWOOD( Handheld Tranceiver's )-TR-2500 TR-2600



( see SMC-25/SMC-30 above. )

KENWOOD-T599S-TS120S-120V-700G-700S-130S-130V-490-520S-530S-820S-830S-
TR2300-TR2200-TR2200GX-TR3200-TR7010-TR7200-TR7200G-TR7400A-TR7500-TR7600-TR7625

PIN1       MIC

PIN2       PTT

PIN3       PTT/EARTH

PIN4       SCREEN AND EARTH

7 PIN REMOTE PLUG/SOCKET.

KENWOOD-TS120-130-140-180-430-440-450-530-570-680-690-830-870-940-950.

PIN1        SPEAKER OUT

PIN2        RELAY COMMON GROUND/EARTH

PIN3        PTT FOR FOOT SWITCH

PIN4        RELAY CLOSED ON TRANSMIT

PIN5        RELAY OPEN ON TRANSMIT

PIN6        ALC INPUT

PIN7        +12VOLTS ON TRANSMIT ( 10 Ma Max )

PLUG        SHELL EARTH.

6 PIN ACC PLUG/SOCKET.

KENWOOD-TS-450-690-570-850-870-950.

PIN1        SIGNAL GROUND/EARTH

PIN2        TRANSMIT DATA

PIN3        RECEIVE DATA

PIN4        CTS ENABLE TX

PIN5        RTS ENABLE RX

PIN6        N/C

SHELL       EARTH

13 PIN ACC2 PLUG.

KENWOOD-TS440-450-680-690-570-711-790-811-850-870-940-950

PIN1         N/C

PIN2         N/C

PIN3         RX AUDIO OUT

PIN4         SCREEN FOR PIN3

PIN5         SQUELCH CONTROL OR N/C

PIN6         S/METER OUTPUT

PIN7         N/C

PIN8         CHASSIS/GROUND

PIN9         PTT- STANDARD MIC INPUT IS MUTED

PIN10        N/C

PIN11        MIC INPUT

PIN12        SCREEN FOR PIN 11

PIN13        PTT- STANDARD MIC INPUT IS ACTIVE

SHELL        EARTH

KENWOOD-TR9000-9030-9130-9300-9500-7700-7730-7750-7800-7850-7930-7950-8400

PIN1        MIC

PIN2        PTT

PIN3        DOWN

PIN6/CENTER EARTH

PIN4        UP

PIN5        NC + 8VOLT SOME MODELS

KENWOOD-TR7600-TR7625

PIN1         MIC

PIN2         PTT

PIN3         N/C

PIN4         CHASSIS/GROUND

PIN5         MIC SCREEN

KENWOOD-TS480 ( 8 Pin modular Plug )

PIN1         UP

PIN2         +8 VOLTS

PIN3         GND

PIN4         PTT

PIN5         MIC GND

PIN6         MIC

PIN7         N/C

PIN8         DOWN

### UPDATE.

Some errors in the TS-480 schematics leading to RF feedback when using other than the stock microphone
have been noted by Kenwood.

MORE INFO TO FOLLOW.

KENWOOD-TS-50-60-140-430-440-450-570-660-670-780-930-430-670-711 TS-811-850-870-930-940-950-440-701-790-680-690-TS-2000
TR-3200-7900-7950-50-751-851
TM-201A-201B-401A-TM401B-211-221-231-241-321-331-3530-421-431-441-521-531-541
TM-621-631-701-721-731-2530-2550-2570
TW4000-4100

PIN1        MIC

PIN2        PTT

PIN3        DOWN

PIN4        UP

PIN5        + 8VOLT Some models ( 10 Ma )

PIN6       (N/C Some models )

PIN7        MIC GROUND.

PIN8        GROUND ( STBY )

KENWOOD-TM-251-255-261-271-271E-451-455-461-641-642-708-732-733-741-742-941-942 ( 8 Pin modular Plug )
TMG-707 TMD-700 TMD700A TMV-71A.TMV-71E-V7A.

KENWOOD PMR TRANCEIVER MODELS-TK-90-7108HM-7108M-7160E-7160HM-7160M-7162E-7180E-7189E
8108HM-8108M-8160E-8160M-8162E-8180E-8189-TK90 ( see KMC-30 /32 /35 above )

PIN1         UP

PIN2         +8 VOLTS (100ma max)

PIN3         GND

PIN4         PTT

PIN5         MIC GND

PIN6         MIC

PIN7         N/C. RX AUDIO (some models)

PIN8         DOWN

KENWOOD-TM-271A ( 8 Pin modular Plug )

PIN1         N/C

PIN2         +8 VOLTS (100ma max)

PIN3         GND

PIN4         PTT

PIN5         MIC GND

PIN6         MIC (600 ohm impedance)

PIN7         N/C

PIN8         KEYPAD SERIAL DATA.

# YAESU.

Further to a telephone call and query to 'YAESU UK' Technical Department today. 18th-APRIL-08.

### PLEASE NOTE:

It is understood from Yaesu that in some cases an alternative cable source was used during the mic manufacturing process
and that microphones of Identical type and model number MAY NOT always have the same color coded connecting cable.

## YAESU MICROPHONES.

YAESU- YM-21. Microphone. 
YAESU- YM-22. Microphone. 
YAESU- YM-34. Microphone 
YAESU- YM-35. Microphone 
YAESU- YM-36. Microphone 
YAESU- YM-37. Microphone 
YAESU- YM-38. Microphone 
YAESU- YM-40. Microphone 
YAESU- YM-47. Microphone. 
YEASU- YM-48. Microphone. 
YAESU- YM-49. Microphone. 
YEASU- YM-50. Microphone. 
YEASU- YM-86. Microphone. 
YAESU- YM-846. Microphone. 
YAESU- YM-2500. Microphone. 
YAESU- YD-148. Microphone. 
YAESU- YD-844. Microphone. 
YAESU- YE-7A. Microphone. 
YAESU- MD-1B8. Microphone. 
YAESU- MD-1C8. Microphone. 
YAESU- MH-1A3B. Microphone. 
YAESU- MH-1B8. Microphone. 
YAESU- MH-10E8 MH-10F8. Microphone. 
YAESU- MH-12A2B. Microphone. 
YAESU- MH-14A8. Microphone. 
YAESU- MH-14B8. Microphone. 
YAESU- MH-14D8. Microphone. 
YAESU- MH-15C8. Microphone. 
YAESU- MH-15D8. Microphone. 
YAESU- MH-18A2B. Microphone. 
YAESU- MH-19A2B. Microphone. 
YAESU- MH-25A8J. Microphone. 
YAESU- MH-26. Microphone. 
YAESU- MH-26G8J.Microphone. 
YAESU- MH-27. Microphone. 
YAESU- MH-27A8J.Microphone. 
YAESU- MH-29A2B. Microphone. 
YAESU- MH-31. Microphone. 
YAESU- MH-31B8. Microphone. 
YAESU- MH-31A8J. Microphone. 
YAESU- MH-32A2B. Microphone. 
YAESU- MH-34 / MH-34B4. Microphone. 
YAESU- MH-34C2B. Microphone. 
YAESU- MH-36. Microphone. 
YAESU- MH-36A6J DTMF Microphone. 
YAESU- MH-36B6JS Microphone. 
YAESU- MH-36D8 Microphone. 
YAESU- MH-36E8J DTMF Microphone. 
YAESU- MH-37A4B Microphone. 
YAESU- MH-42. Microphone. 
YAESU- MH-42A6J Microphone. 
YAESU- MH-42B6JS Microphone. 
YAESU- MH-42B6J Microphone schematic.pdf 
YAESU- MH-44A4B Microphone. 
YAESU- MH-48. Microphone. 
YAESU- MH-48A6J. Microphone. 
YAESU- MH-57A4B.Microphone. 
YAESU- MH-59A8J.Microphone. 
YAESU- MH-61A8J.Microphone. 
YAESU- MH-64A8J.Microphone. 
YAESU- MH-67A8J.Microphone. 
YAESU- MH-68A8J.Microphone. 
YAESU- MH-700D. Microphone. 
YAESU- MD-11A8J. Microphone. 
YAESU- MD-100. Microphone. 
YAESU- MD-100A8X. Microphone. 
YAESU- MD-100/100AX schematic.pdf 
YAESU- MD-200. Microphone. 
YAESU- MD-200A8X. Microphone. 
YAESU- MD-200.Instruction Manual.pdf 

YAESU MICROPHONE COMPATIBILITY LIST.

YAESU STANDARD MICROPHONE LIST.

MORE YAESU MICROPHONE INFO. 

YAESU TNC INFORMATION.

YAESU ( Handheld Tranceiver's ) VX-1R VXF-1 VX-2R VX-2E VX-3R VX-5R VX-7R VX-10 VXF-10 VX-110
VX-130 VX-131 VX-132 VX-150 VX-160 VX-180 VX-210 VX-210A VX-300 VX-400 VX-410 VX-420 

    ( see MH-34 / MH-34B4 / MH-57A4B ABOVE )

YAESU ( Airband Tranceiver's ) VXA-100 VXA-150 VXA-210 

    ( see MH-44A4B ABOVE )

YAESU ( Handheld Tranceiver's ) FT-10R FT-40R FT-50R FT-60R 

     ( see MH-37A4B ABOVE )

YAESU FT-50R FT-60R

YAESU ( Handheld Tranceiver's ) FT-51R ( see MH-32A2B / MH-34C2 )

YAESU ( Handheld Tranceiver's ) FT-51RII

YAESU ( Handheld Tranceiver's ) FT-470 FT-411 FT-811 FT-911 ( see MH-32A2B / MH-34C2 )

YAESU ( Handheld Tranceiver's ) FT-23 FT-73 FT-23RII FT-73RII ( see MH-32A2B / MH-34C2 ) 



CLONE INFO. pdf

YAESU ( Handheld Tranceiver's ) FT-530 ( see MH-12A2B / MH-18A2B )

YAESU POLICE AND PUBLIC SAFETY CHANNELISED TRANCEIVERS
VX-2000 VX-2500 VX-3000 VX-3200 VX-4100 VX-4100E VX-4200 VX-4200E VXR-1000 VXR-7000

(See MH-25A8J / MD-11A8J microphones above )

PIN1        FAST

PIN2        GROUND

PIN3        PTT

PIN4        MIC

PIN5        MIC EARTH

PIN6        + 5VOLTS

PIN7        UP

PIN8        DOWN

YAESU-FT736-FT747GX-FT757GX-FT650-FT655-FT840-FT890-FT920-FT990-FT990D-FT847
FT1000-FT1000D-FT1000MP + MKV -FT2000

PIN1        MIC UP

PIN2        EARTH ( + 5VOLTS FT847-FT920-FT1000MP-FT2000 )

PIN3        DOWN

PIN4        FAST SCAN

PIN5        EARTH

PIN6        PTT

PIN7        SCREEN/EARTH

PIN8        MIC

YAESUFTONE-FT77-FT102-FT707-FT767-FT767GX-FT980

PIN1        MIC UP

PIN2        + 5 VOLTS

PIN3        DOWN

PIN4        FAST SCAN

PIN5        CAUTION INTERCONNECTED TO PIN 2.( +5 VOLTS )

PIN6        PTT

PIN7        SCREEN/EARTH

PIN8        MIC

YAESU FT480R-FT780R ( see YM-40 above )

PIN1 green       MIC UP

PIN2 yellow      EARTH / COMMON U/DOWN.

PIN3 blue        DOWN

PIN4 brown       TONE CALL / LOCK

PIN5 orange      EARTH TONE CALL / LOCK

PIN6 red         PTT

PIN7 black       SCREEN/EARTH

PIN8 white       MIC

YAESU-FT726 (see MD1-B8 MH1-B8 Microphone above)

PIN1        UP

PIN2        COMMON UP/DOWN

PIN3        DOWN

PIN4        FAST SCAN

PIN5        EARTH

PIN6        PTT

PIN7        SCREEN/EARTH

PIN8        MIC

YAESU CPU2500R-CPU2500RK SOMMERKAMP FT227
(see YM-2500 Microphone above)

PIN1       UP

PIN2       COMMON UP/DOWN

PIN3       DOWN

PIN4       PTT

PIN5       GROUND MIC/PTT

PIN6       MIC

click for schematic

YAESU FT-620B 
(see YM-86 Microphone above)

PIN1       N/C

PIN2       N/C

PIN3       SCREEN

PIN4       PTT GROUND

PIN5       PTT

PIN6       MIC

click for schematic

YAESU FT75-FT221R-FT223-FT101B-FT101E-FT101Z-FT101ZD-FT301D-FT902-FT902DM. ( see YD148/YD844 microphone above.)

PIN1       MIC SCREEN/EARTH ( PTT EARTH ON FT101B/101E.FT101Z/101ZD.FT902/902DM.)

PIN2       MIC

PIN3       PTT

PIN4       EARTH ON FT221R.( N/C ON FT101Z/101ZD.FT101B/101E.FT902/902DM. )

YAESU FTDX-100 FTDX-400 FTDX-401 FTDX-560 FT-200 FT-250( See YD-148 microphone above.)

YAESU FT201-FT125C-FTC212-FT2B-FT300C-FT224-FT225RD-FT2FB-FT223-FT220-FTC212-FT300C FT301.
FT7-FT227R-FT227RA-FT227RX-FT250-FT401B-FT501-FT625-FL101.

( See YD-148 and YM-22 microphones above.)

YAESU-FT950

PIN1        MIC UP

PIN2        + 5 VOLTS

PIN3        DOWN

PIN4        FAST SCAN

PIN5        GROUND

PIN6        PTT

PIN7        SCREEN/EARTH

PIN8        MIC

YAESU FT840-FT990.

PIN1       UP

PIN2       GROUND

PIN3       DOWN

PIN4       FAST

PIN5       GROUND (INTERCONNECTED ON TRANCEIVER TO PIN 2. )

PIN6       PTT

PIN7       MIC GROUND/SCREEN

PIN8       MIC

YAESU FT2200.

PIN1       UP

PIN2       + 5 VOLTS

PIN3       DOWN

PIN4       SPEAKER.

PIN5       ACC.

PIN6       PTT

PIN7       MIC GROUND/SCREEN

PIN8       MIC

YAESU FT2500M.
8 Pin Modular plug.( see MH-26G8J MH-27G8J )

PIN1       CALL BUTTON.

PIN2       RX AUDIO.

PIN3       PTT.

PIN4       MIC.

PIN5       GROUND.

PIN6       + 5 VOLTS

PIN7       UP.

PIN8       DOWN.

YAESU FT2400H.

PIN1       CALL BUTTON.

PIN2       RX AUDIO.

PIN3       PTT.

PIN4       MIC.

PIN5       GROUND.

PIN6       + 5 VOLTS

PIN7       UP.

PIN8       DOWN.

YAESU-FT-2600( 6 Pin modular Plug )( See MH-42 and MH-36 microphone above )

PIN1         SW2

PIN2         CLONE

PIN3         + 9VOLT

PIN4         GROUND

PIN5         MIC

PIN6         MULTI SWITCHING SW1

YAESU FT5100.

PIN1       UP.

PIN2       + 5 VOLTS.

PIN3       DOWN.

PIN4       SPEAKER.

PIN5       BAND.

PIN6       PTT.

PIN7       EARTH.

PIN8       MIC.

YAESU FT211-FT212R FT212RH-FT270-FT211RH-FT711-FT712-FT770-FT2311-FT2700-FT4700RH-FT711RH-FT770RH 
(see microphones MH-15D8/ MH-15C8/ MH-14A8/ MH-14B8/ MH-14D8 above )

PIN1       UP

PIN2       +5 VOLT

PIN3       DOWN

PIN4       SPEAKER

PIN5       CPU/ TONE SW

PIN6       PTT

PIN7       GROUND

PIN8       MIC

YAESU FT230R-FT290R-FT690 FT730-FT790R

PIN1       MIC SCREEN/EARTH

PIN2       MIC

PIN3       PTT

PIN4       + 12VOLT ( + 5 VOLTS FT730-FT290R )

PIN5       SPEAKER

PIN6       UP

PIN7       DOWN

YAESU FT290RII-FT690RII-FT790RII (see MH-10E8 /MH-10F8 above )

PIN1       UP

PIN2       + 5 VOLTS

PIN3       DOWN

PIN4       SPEAKER

PIN5       N/C

PIN6       PTT

PIN7       GROUND

PIN8       MIC

YAESUFT215-FT715-FT3700-FT3800-FT3900-FT4600-FT4800-FT4900-FT5800

PIN1       UP

PIN2       + 5 VOLTS

PIN3       DOWN

PIN4       N/C

PIN5       RECALL

PIN6       RESET

PIN7       GROUND

PIN8       MIC

YAESU FT708R-FT208R HAND HELD.
( mini ) 6 PIN

PIN1        MIC ( white )

PIN2        SPEAKER ( black )

PIN3        PTT ( red )

PIN4        MIC SCREEN

PIN5        NC

PIN6        SPEAKER ( blue )

YAESU-FT897-FT857-FT817-FT900-FT-450 ( 8 pin Modular Plug )

PIN1         FAST SCAN

PIN2         GROUND

PIN3         PTT

PIN4         MIC

PIN5         MIC GROUND

PIN6         + 5VOLT

PIN7         UP

PIN8         DOWN

YAESU-FT1500-FT1802E-FT2800-FT7800M-FT8800E-FT8900R ( 6 Pin modular Plug )( See MH-48 microphone above )

PIN1         SW2

PIN2         SW1

PIN3         + 8VOLT

PIN4         GROUND

PIN5         MIC

PIN6         PTT (clone FT1802E )

YAESU-FTM-10R/E ( WITH BUILT IN MICROPHONE AND BLUE TOOTH.) 

NEEDS MEK-M10 ADAPTER TO USE THE FOLLOWING EXTERNAL MICROPHONES

MH-68 A6J WATERPROOF MIC

MH-68 B6J WATERPROOF MIC

MEK-M10 ADAPTER CONNECTIONS.pdf

YAESU-FTDX9000D ( 3 pin XLR Plug front panel) PLUS ( 8 pin Plug rear panel.)

( XLR PLUG FRONT PANEL.)

PIN1        MIC GRND.

PIN2        MIC HOT.

PIN3        MIC COLD.

( 8 PIN PLUG REAR PANEL.)

PIN1        UP.

PIN2        +5 VOLTS.

PIN3        DOWN.

PIN4        FAST SCAN.

PIN5        GROUND.

PIN6        PTT.

PIN7        MIC GROUND.

PIN8        MIC.

YAESU-FT100-FT90-FT8100 ( 6 pin Modular Plug ) (SEE MH-36 microphone above.)

PIN1         Multi-function switching for P,P1,P2 SW2.

PIN2         N.C. 9600bps packet data out FT-90

PIN3         + 9VOLT

PIN4         EARTH

PIN5         MIC.

PIN6         SW1.PTT,UP,DOWN,Acc

Yaesu "cat"pinout connections.

### MORE YAESU INFORMATION

(click for) -YAESU FT-100 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-600 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-707 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-726 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-736 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-747 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-757 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-767 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-817 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-847 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-897 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-920 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-980 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-990 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FTM-10 SERIES CONNECTION DIAGRAMS.pdf 
(click for) -YAESU FT-1000MP SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-2000 SERIES CONNECTION DIAGRAMS.pdf
(click for) -YAESU FT-7100 SERIES CONNECTION DIAGRAMS.
(click for) -YAESU FT-8900 SERIES CONNECTION DIAGRAMS.pdf
(click for)-YAESU FTDX-9000D SERIES CONNECTION DIAGRAMS.

# ICOM.

ICOM-IC7400-IC746-IC746PRO-IC756PRO-IC7700-IC7800 (see HM-36 below )

PIN1       MIC + DC VOLTS FOR ICOM ONLY MICROPHONE

PIN2       + 8VOLTS 10Ma TO AVOID DAMAGING THE REGULATOR DO NOT SHORT TO GROUND

PIN3       UP/DOWN

PIN4       SQUELCH

PIN5       PTT

PIN6       GROUND

PIN7       MIC SCREEN/EARTH

PIN8       AUDIO OUT

ICOM-IC703-IC706MK1-IC706MK2-IC706MK3-IC2000-IC2000H (8 Pin Modular Plug )

PIN1       + 8VOLT

PIN2       UP/DOWN

PIN3       AUDIO OUT

PIN4       PTT

PIN5       MIC GROUND

PIN6       MIC

PIN7       GROUND/EARTH

PIN8       SQUELCH

ICOM-ICE-208-IC2100H-IC2200H-IC2725E-IC2820-(See HM-133 below ) (8 Pin Modular Plug )

PIN1       + 8VOLT OUTPUT ( 10 ma max )

PIN2       UP/DOWN

PIN3       + 8VOLTS IN ( No connection IC2100H )

PIN4       PTT

PIN5       MIC GROUND

PIN6       MIC

PIN7       GROUND/EARTH

PIN8       DATA IN ( No connection IC2100H )

ICOM-IC-7000 (8 Pin Modular Plug )

#### IMPORTANT! SEE HM-151 MICROPHONE INFO BELOW.

PIN1       + 8VOLT OUTPUT ( 10 ma max )

PIN2       UP/DOWN

PIN3       + 8VOLTS SW

PIN4       PTT

PIN5       MIC GROUND

PIN6       MIC

PIN7       GROUND/EARTH

PIN8       DATA IN

ICOM-IC-2800 (8 Pin Modular Plug ) SEE HM-98 MICROPHONE BELOW.

PIN1       + 8VOLT OUTPUT ( 10 ma max )

PIN2       UP/DOWN

PIN3       + 8VOLTS SW

PIN4       PTT

PIN5       MIC GROUND

PIN6       MIC

PIN7       GROUND/EARTH

PIN8       DATA IN

ICOM-IC-2800 (8 Pin Modular Plug ) SEE HM-98 MICROPHONE BELOW.

PIN1       + 8VOLT OUTPUT ( 10 ma max )

PIN2       UP/DOWN

PIN3       + 8VOLTS SW

PIN4       PTT

PIN5       MIC GROUND

PIN6       MIC

PIN7       GROUND/EARTH

PIN8       DATA IN

ICOM LAND MOBILE(8 Pin Modular Plug ) SEE SM-25 SM-100/T MICROPHONES BELOW.
F320-F420-F1020-F2020-F121-F221-F521-F620-F621/TR-F1721D-F182D-F272D
F282D-FR3000-FR4000-FR5000-FR5100-FR6100.

PIN1       + 8 VOLTS

PIN2       UP/DOWN.

PIN3       AF OUTPUT.

PIN4       PTT.

PIN5       MIC GROUND.

PIN6       MIC AUDIO.

PIN7       GROUND/EARTH.

PIN8       SQUELCH ( SOME MODELS )

ICOM HAND HELD- ICE90- IC91A/E- ICE7- ICT2A/E/H-ICT3H ICT7A/E/H- ICT21A/E -ICT22 -ICT41E- ICT81A/E- ICV8- ICV21AT- ICV82
ICV82- ICT90- ICF3 

( SEE HM-46 HM75A HM-131 BELOW )

ICOM HAND HELD- IC4A/AT/E-IC3A/AT-IC12A/AT/E-IC80AD

ICOM HAND HELD- ICT8A- ICT8E

ICOM-IC-211 IC-701

PIN1       MIC

PIN2       PTT

PIN3       N/C

PIN4       GROUND.

ICOM IC-120-271A-271E-275-290-228-229-229H-22U-25-25E-27-27E-28-29E-255-260-290-2400-2500-3200-3210-3220
IC-37A-38A-375-45-47-77-78-451-471A-475-48-490-505-551-560-575-707-718-720-725-726-728-729-730-735-736-737/A-738
IC-740-745-746-751/A-756/PRO-761-765-775-781-820H-821-821H-900-901-901H-910X-970-1200-1201-1271-1275

PIN1       MIC (yellow)

PIN2       REPEATER TONE (+ 8/9 volts some models)

PIN3       UP/DOWN

PIN4       N/C (squelch some models )

PIN5       PTT(red)

PIN6       EARTH (black)

PIN7       MIC SCREEN

PIN8       N/C (green)(external speaker some models )

( For IC-27 / 27E see IC-HM24 below ) (IC-22U see IC-HM8 below)

ICOM-IC24G-IC251E-IC451E. (See SM-5 plus IC-HM7 hand mic & SM-5 desc mic.)

PIN1       MIC ( white. connection at + 9VOLTS  above earth )

PIN2       NC

PIN3       NC

PIN4       NC

PIN5       PTT ( red )

PIN6       PTT ( black )

PIN7       MIC SCREEN

PIN8       NC

## ICOM MICROPHONES.

ICOM- SM2 MIC CONNECTIONS.
ICOM- SM5 MIC CONNECTIONS.
ICOM- SM6 MIC CONNECTIONS.
ICOM- SM8 MIC CONNECTIONS.
ICOM- SM10 MIC CONNECTIONS.
ICOM- SM20 MIC CONNECTIONS.
MORE- SM20 MIC INFORMATION.
ICOM- SM25 MIC CONNECTIONS.
ICOM- IC-HM5 MIC CONNECTIONS.
ICOM- IC-HM7 HAND MIC CONNECTIONS.
ICOM- IC-HM8 HAND MIC CONNECTIONS.
ICOM- IC-HM10 MIC CONNECTIONS.
ICOM- IC-HM11 MIC CONNECTIONS.
ICOM- IC-HM12 MIC CONNECTIONS.
ICOM- HM12 MIC CONNECTIONS.
MORE- IC-HM12 MIC INFORMATION.
ICOM- IC-HM14 MIC CONNECTIONS.
ICOM- IC-HM15 MIC CONNECTIONS.
ICOM- HM-22 MIC CONNECTIONS.
ICOM- HM-23 MIC CONNECTIONS.
ICOM- HM-24 MIC CONNECTIONS.
ICOM- HM-36 MIC CONNECTIONS.
ICOM- HM-46 MIC CONNECTIONS.
ICOM- HM-54 MIC CONNECTIONS.
ICOM- HM-56/56A MIC CONNECTIONS.
ICOM- HM-75A MIC CONNECTIONS.
ICOM- HM77-HM78-HM79-HM95-HM97 MIC CONNECTIONS.
ICOM- HM-90 WIRELESS MIC CONNECTIONS.
ICOM- HM-95 MIC CONNECTIONS.
ICOM- HM-96 MIC CONNECTIONS.
ICOM- HM-97 MIC CONNECTIONS.
ICOM- HM-98S MIC CONNECTIONS.
ICOM- HM-100 HM-100T MIC CONNECTIONS.
ICOM- HM-103 MIC CONNECTIONS.
ICOM- HM-113-113V MIC CONNECTIONS.
ICOM- HM-128L MIC CONNECTIONS.
ICOM- HM-118-118TN MIC CONNECTIONS.
ICOM- HM-131 MIC CONNECTIONS.
ICOM-HM-148/G MIC CONNECTIONS.
ICOM- HM-133 MIC CONNECTIONS. 
ICOM- HM-151 MIC CONNECTIONS (IC-7000 ).
ICOM- HM-152 MIC CONNECTIONS.
ICOM- HM-153L MIC CONNECTIONS.
ICOM- HM-154 / HM-154T MIC CONNECTIONS. 
CONVERTING THE ICOM- HM-154 / HM-154T MIC FROM RJ-45 TO 8 PIN CONNECTIONS. 
ICOM- HM-158L MIC CONNECTIONS.
ICOM- HM-166L MIC CONNECTIONS.
IC-821H- ACC SOCKET CONNECTIONS.


click for MORE ICOM INFORMATION.
click for ICOM MICROPHONE COMPATIBILITY LIST 2009
click for ICOM CONNECTING CABLE REFERENCE LIST.
click to download FREE ICOM MANUALS.

CAUTION !

IF YOU WISH TO USE THE FOLLOWING ICOM MICROPHONE'S ( model's below ) ON

TRANCEIVERS OTHER THAN ICOM, CHECK THIS   link    INFORMATION ALSO

MICROPHONE MODEL'S 

IC-SM8 IC-SM6 IC-HM7 IC-HM11 IC-HM12 IC-HM14 IC-HM15 IC-HM22 IC-HM24 IC-HM36

# ALINCO.

Click here to Download ALINCO Instruction/Service manuals FREE.

ALINCO DX70-DX70T-DX77-DX701-DX707-DR110-DR112-DR119-DR135-DR-330 DR435-DR150E-DR150TE-DR235-DR-410-DR430-DR435-DR510-DR570
-DR590-DR592T-DR599T-DR600T-DR610-DR620-DR635-DR1200-DRM03-DRM06-ALR22H-ALD24T-ALR22T-ALR72T-

PIN1       MIC

PIN2       PTT

PIN3       DOWN

PIN4       UP

PIN5       + 5VOLT ( Max current 25Ma )( + 8VOLT ALR-22/24 )

PIN6       AUDIO OUT ( remote DR150TE-DR590-DR592-DR599-DR600 ) SEE ABOVE DIAGRAM REFERENCE.

PIN7       MIC SCREEN/EARTH

PIN8       EARTH

ALINCO DR140-DR605 ( Modular Plug )

PIN1        UP.

PIN2        GROUND.

PIN3        MIC.

PIN4        MIC GROUND.

PIN5        PTT.

PIN6        N/C.

PIN7        DOWN.

PIN8        + 5 VOLTS.

ALINCO 22T/E.24E/T

PIN1         MIC

PIN2         PTT

PIN3         DOWN

PIN4         UP

PIN5         + 8VOLT

PIN6         N/C

PIN7         MIC EARTH

PIN8         GROUND

ALINCO EMS-14. - ADONIS AM-508E. -WATSON AM308 MICROPHONE COLOR CODING.

YELLOW   MIC

SCREEN   EARTH (ground)

GREY     PTT ( + VOLTAGE FEED ON ADONIS D80 )

BLUE     PTT EARTH ON WATSON 308.

PURPLE   PTT EARTH (ground)

GREEN    MIC UP

ORANGE   COMMON (connect to ground)

WHITE    MIC DOWN ( + VOLTS WATSON AM-308 )

BLACK    MIC DOWN ON WATSON AM-308

RED      + VOLTS FEED( PTT ON ADONIS D80 AND WATSON AM-308 )

ALINCO DMR610 DR-135 DR-435.

PIN 1    MIC

PIN 2    PTT

PIN 3    DOWN

PIN 4    UP

PIN 5    +5 VOLTS

PIN 6    REMOTE CONTROL

PIN 7    SCREEN   EARTH (ground)

PIN 8    GND

ALINCO. DJ-S11 DJ-41 DJ-180 DJ-190 DJ-191 DJ-491G DJ-G1 DJ-G5

ALINCO. DJ-560 DJ-580

ALINCO HANDHELD. DJ-V17 DJ-V17E DJ-V17T DJ-V17TFH DJ-47E DJ-47T DJ-47T1 DJ-47T2 

click for schematic

## ALINCO MICROPHONES

EMS-5A MIC CONNECTIONS.
EMS-14 MIC CONNECTIONS.
EMS-42.MIC CONNECTIONS.
EMS-45.MIC CONNECTIONS.
EMS-46.MIC CONNECTIONS.
EMS-47.MIC CONNECTIONS.
EMS-51.MIC CONNECTIONS.
EMS-52.MIC CONNECTIONS.
EMS-53.MIC CONNECTIONS.
EMS-52 / 53.MIC SCHEMATICS.
EMS-54.MIC CONNECTIONS.
EMS-55.MIC CONNECTIONS.
EMS-54 / 55.MIC SCHEMATICS.
EMS-56.MIC CONNECTIONS.
EMS-56.MIC SCHEMATIC.
EMS-57.MIC CONNECTIONS.
EMS-57.MIC SCHEMATIC.

## ADONIS.

ADONIS- AM-DX1 MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- AM-308 MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- AM-503G MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- AM-508e MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- AM-708 MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- AM-7500e MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- AM-308 / AM-508 / AM-608 / AM-708 / AM-7500E MICROPHONE PHOTO'S
ADONIS- FX-6 MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- WX-2400 MICROPHONE INSTRUCTIONS AND SCHEMATIC.pdf
ADONIS- BOOM1 MICROPHONE CONNECTIONS.pdf

ADONIS MICROPHONE INTERCONNECTING CABLE INFO.

INFO TO CONNECT ADONIS AM-DX1 AM-308 AM-508 AM-708 AM-7500e TO YAESU FT-847 FT-920 FT-1000MP.

ADONIS MICROPHONE CONVERTION LEADS FOR AM-708 ABOVE.

ADONIS LEAD NUMBER D-88K AS-327 ( Connections for Kenwood configuration)

SILVER PLUG END (tranceiver).     ORANGE PLUG END ( connected to microphone).

PIN 1  YELLOW.     connected to   PIN 2.YELLOW.(mic)

PIN 2  RED.            ..         PIN 3.RED.(ptt)

PIN 3  WHITE.          ..         PIN 6.WHITE.(down)

PIN 4  GREEN.          ..         PIN 5.GREEN.(up)

PIN 5  GREY.           ..         PIN 8.GREY.(+volts DC feed)

PIN 6  N/C.            ..         PIN 4.PURPLE.(ptt ground)

PIN 7  SCREEN.         ..         PIN 1.SCREEN.(mic ground)

PIN 8  ORANGE+PURPLE.  ..         PIN 7.ORANGE.(up/down common ground)

ADONIS LEAD NUMBER D-80K AS-340 
This is sold as a spare lead with only orange (mic end) plug fitted.

ORANGE PLUG END (connected to microphone).

PIN 2.YELLOW.(mic)

PIN 3.RED.(ptt)

PIN 6.WHITE.(down)

PIN 5.GREEN.(up)

PIN 8.GREY.(+volts DC feed)

PIN 4.PURPLE.(ptt ground)

PIN 1.SCREEN.(mic ground)

PIN 7.ORANGE.(up/down common ground)

COLOURS AND CONNECTIONS ON THE ORANGE (mic) PLUG ENDS OF LEADS ARE IDENTICAL.

STANDARD ADONIS MICROPHONE COLOR CODING

YELLOW. (mic)

RED. (ptt)

WHITE. (down)

GREEN. (up)

GREY. (+volts DC feed)

PURPLE. (ptt ground)

SCREEN. (mic ground)

ORANGE. (up/down common ground)

## ADI.

ADI. AR-146 AR-147 AR-247 AR-446 AR-447 

8 PIN ROUND PLUG.

PIN 1     MIC.

PIN 2     PTT.

PIN 3     DOWN.

PIN 4     UP.

PIN 5     + 8VOLTS ( max 150 Ma ).

PIN 6     RX AUDIO OUT.

PIN 7     MIC SCREEN.

PIN 8     GROUND.

## AEA.

AEA. DX-HANDY 6M,DX-HANDY 10M

## ALBRECT.

AE485 MIC SCHEMATIC.

AE497 MIC SCHEMATIC.

AE560 MIC SCHEMATIC.

## AKD/GAREX.

AKD/GAREX. 2001-4001-6001-7003 

4 PIN PLUG.

PIN 1     MIC.

PIN 2     COMMON EARTH.

PIN 3     AUDIO OUTPUT.

PIN 4     PTT.

## ASTATIC.

ASTATIC 531 schematic.

ASTATIC D104 schematic.

ASTATIC MICROPHONE WIRING REFERENCE pdf

## ATLAS.

ATLAS TRANCEIVERS MODELS.-TX110-180-210-215-350XL.
ATLAS-VX5 VOX UNIT.

## AZDEN.

PCS-5000-6000-7000-7200-7300-7600-7800-9600

PIN 1     MIC.

PIN 2     MIC GROUND.

PIN 3     TONE BURST (connect to pin 6)

PIN 4     DOWN.

PIN 5     UP.

PIN 6     COMMON GROUND.

PIN 7     PTT.

PIN 8     +13.8 VOLTS

AZDEN-PCM-463 MICROPHONE INFO.

## CES MICROPHONES.

CES-600L MICROPHONE.pdf

CES-805 MICROPHONE.pdf

## COLLINS.

KMW-1 KWM-2 KWM-2A KWM-380 KWM-390, 312B-4, 312B-5, (S-LINE) 32S-1.



COLLINS SM1/SM3 MICROPHONE INFO.

COLLINS 32V KW-1 KWS-1

PIN 1 MIC AUDIO.
PIN 2 PTT.
CASE COMMON GROUND/EARTH

COLLINS 32RA.

PIN 1 COMMON GROUND/EARTH.
PIN 2 PTT.
PIN 3 MIC AUDIO.

## DRAKE.

DRAKE. TR-5 TR-7 TR-7A 

4 PIN PLUG.

PIN 1     MIC.

PIN 2     PTT.

PIN 3/4   EARTH/GROUND.

DRAKE. TR-22 

3 PIN LOCKING RING TYPE PLUG.

PIN 1     MIC.

PIN 2     PTT.

PIN 3     EARTH.

DRAKE. TR-72 

4 PIN PLUG.

PIN 1     MIC.

PIN 2     PTT.

PIN 3/4   EARTH/GROUND.

DRAKE. TR-270 

4 PIN PLUG.

PIN 1     MIC.

PIN 2     PTT.

PIN 3     COMMON EARTH.

PIN 4     + 10 VOLTS

DRAKE. TR-3 T4 TR-4 TR-4B TR-4XB TR-4XC TR-4C T-4XC T-4XB TR-6

( S230 Mic Plug.)

## ELECRAFT.

K3

PIN 1     MIC.

PIN 2     PTT.

PIN 3     DOWN

PIN 4     UP.

PIN 5     FUNCTION.

PIN 6     8 VOLTS.

PIN 7     GROUND.

PIN 8     GROUND.

## FDK.

FDK. MULTI-11 MULTI-UII MULTI-II MULTI-700E MULTI-700EX MULTI-800 MULTI-2000 MULTI-2700 

4 PIN ROUND PLUG.

PIN 1/4   GROUND / MIC SREEN

PIN 2     PTT.

PIN 3     MIC.

FDK. MULTI-750A MULTI-750E MULTI-725 

6 PIN ROUND PLUG.

PIN 1     MIC

PIN 2     PTT.

PIN 3     UP.

PIN 4     + 5V

PIN 5     GROUND.

PIN 6     DOWN.

## HALLICRAFTER.

HT-46

HALLICRAFTER. HT-32 HT-36 HT-44 SR-42 SR-42A SR-46 SR-150 SR-160 SR-400 SR-400A SR-500 SR-540 SR-2000

HALLICRAFTER. HT-40 HT-37

## HEATHKIT.

Heathkit- SB-100 / SB-104 mic Connection 

Heathkit- HW-12 / HW-22 mic Connection 

Heathkit- HW-17 mic Connection

## HEIL.

HM-10 DUAL, GM-4,GM-5,GMV. HANDIMIC-HM-4, HM-5, HM-iC, HM-PRO. CLASSIC.
4 PIN XLR PLUG.

PIN 1    GROUND/SHIELD.

PIN 2    MIC.

PIN 3/4  PTT.

PRO-20, PRO-30, PR0-40, CLASSIC PRO, HERITAGE.
3 PIN XLR PLUG.

UNBALANCED OUTPUT.

PIN 1    SHIELD.

PIN 2    + MIC.

PIN 3    - MIC.( connected to pin 1 )

BALANCED OUTPUT.

PIN 1    SHIELD.

PIN 2    + MIC OUTPUT

PIN 3    - MIC GROUND

HEIL TRAVELER HEADSET

PIN 1    MIC.

PIN 2    +8 VOLTS.

PIN 3    U/DOWN.

PIN 4    SQUELCH.

PIN 5    PTT.

PIN 6    EARTH PTT.

PIN 7    MIC EARTH.

PIN 8    AUDIO OUTPUT.

THE HEIL CONNECTION SYSTEM.

MORE INFORMATION FROM THE HEIL WEBSITE.

## JCD-201M DESK MIC.

PIN1 (E) BRAID.

PIN2 (M) (MIC)   BROWN

PIN3 (P) (GROUND) WHITE

PIN4 (G) (PTT) GREEN

PIN5 (U) (UP) BLACK

PIN6 (D) (DOWN) YELLOW

PIN7 (C) (UP/DOWN EARTH) BLUE

PIN8 (B) (+5 - +9VOLTS DC) RED

JCD-201M PHOTO.

## JRC.

JST-100 JST-100D JST-100S JST-110 JST-135 JST-145 JST-245.

PIN1        MIC UP

PIN2        NC

PIN3        MIC DOWN

PIN4        + 9 VOLTS

PIN5        PTT EARTH

PIN6        PTT

PIN7        MIC EARTH

PIN8        MIC

NVT-56 / 57 / 58 MICROPHONE INFO.

## KACHINA.

KACHINA. 505DSP. 

8 PIN ROUND PLUG.

PIN 1     GROUND.

PIN 2     MIC.

PIN 3     PTT.

PIN 4     SPEAKER.

PIN 5     N/C.

PIN 6     N/C.

PIN 7     N/C.

PIN 8     N/C.

( info AE5K )

## KDK.

KDK. FM-2016 FM-2025 

4 PIN ROUND PLUG.

PIN 1     PTT GROUND.

PIN 2     PTT.

PIN 3     MIC SCREEN.

PIN 4     MIC.

KDK. FM-2030 FM-2033 

6 PIN ROUND PLUG.

PIN 1     UP/DOWN GROUND.

PIN 2     UP.

PIN 3     DOWN.

PIN 4     PTT.

PIN 5     MIC.

PIN 6     MIC SREEN/GROUND.

KDK DM-TT1 MICROPHONE 

KDK TM-2 MICROPHONE 

KDK DM-100 MICROPHONE

## KW.

KW TRANSMITTERS /TRANCEIVERS KW-1 KW-2000 KW-2000A KW-2000B KW-VESPA KW-VICEROY

## MFJ.

MFJ-8621. DATA CONNECTIONS. Must be configured for 1200 baud operation.

Note:This radio has un-squelched output.use "software DCD"

PIN1       AFSK In (yellow)

PIN2       GROUND/EARTH (black)

PIN3       PTT (red)

PIN4       AFSK Out (green)

MFJ-297 MFJ-299 MICROPHONES.

PIN1       MIC GROUND

PIN2       MIC

PIN3       PTT

PIN4       PTT GROUND

PIN5       UP

PIN6       DOWN

PIN7       COMMON UP/DOWN

PIN8       DC VOLTS.

MFJ-299 INSTRUCTION MANUAL WITH ( ICOM,YAESU,KENWOOD,CONNECTION INFO.)


MFJ-434 VOICE KEYER INFO.pdf

DOWNLOAD MFJ PRODUCT MANUALS FREE.

## MOTOROLA.

CM140-160-200-300-340-360 EM200-400 GM300-3188-3688.
M10-120-130-208-216-1255-1255LS-MaxTrac PM400-SM120-SM50.

PIN1        N/C

PIN2        N/C

PIN3        GROUND (blue)

PIN4        GROUND (black)

PIN5        MIC (red)

PIN6        PTT (green)

PIN7        N/C (yellow)

PIN8        AUDIO (blue)

HMN-1035 MIC SCHEMATIC.pdf

## NAVICO.

AMR-1000/S.

PIN1        MIC GROUND 0VOLTS

PIN2        PHONES

PIN3        CRADLE

PIN4        PTT

PIN5        MIC

PIN6        +12 VOLTS

PIN7        DOWN

PIN8        UP

## NEC.

NEC. CQ110E 

4 PIN ROUND PLUG.

PIN 1+4   ( INTERCONNECTED ) GROUND / MIC SREEN

PIN 2     PTT.

PIN 3     MIC.

## RADIO SHACK.

RADIO SHACK. ( Modular Connector)

Models HTX-212.HTX242.

PIN2       GROUND/EARTH (black)

green      EXTERNAL SPEAKER

PIN5       MIC (yellow)

PIN6       PTT (red)

RADIO SHACK- HTX-100 MICROPHONE INFO.

RADIO SHACK- HTX-242 MICROPHONE SCHEMATIC.

RADIO SHACK- HTX-252 MICROPHONE INFO.(pdf )

## SGC.

SG-2020.

PIN 1     MIC.

PIN 2     PTT.

PIN 3     OPT 1.

PIN 4     OPT 2.

PIN 5     N/C.

PIN 6     RX AUDIO OUT.

PIN 7     MIC GROUND.

PIN 8     GROUND.

## SOMMERKAMP

TS-280FM TS-480FM.

SOMERKAMP

FT-307CBM (see YAESU FT-107 )

FT-277ZD ( see YAESU FT-101ZD )

FT-767DX ( see YAESU FT-707 )

FT-7B ( see YAESU FT-7 )

## STANDARD.

C58-C78-C88-C1100-C4100-C5800-C7800-C8800-C8900

PIN 1     MIC.

PIN 2     PTT.

PIN 3     SPEAKER.

PIN 4     COMMON (NOTE:+8VOLTS ON THIS CONNECTION.)

PIN 5     DOWN.

PIN 6     UP.

PIN 7     GROUND.

Note.0.001uF capacitor is connected between pin 1 and pin 7

STANDARD.
C5000-C5200-C6000-C6000S

PIN 1     MIC.

PIN 2     PTT.

PIN 3     SPEAKER.

PIN 4     COMMON.

PIN 5     UP.

PIN 6     DOWN.

PIN 7     CALL.

PIN 8     GROUND.

C5608

PIN 1     MIC.

PIN 2     PTT.

PIN 3     SPEAKER.

PIN 4     + 7.5 VOLTS.

PIN 5,6,7 MICROPROCESSOR INTERFACE PINS.

PIN 8     GROUND.

STANDARD.
C5900 ( 8 pin modular type plug.)

PIN 1

PIN 2

PIN 3

PIN 4     PTT.

PIN 5     GROUND.

PIN 6     MIC.

PIN 7

PIN 8

## SWAN.

SWAN.100MX-120-100SS-140-175-200A-240-250C-350-400-500-500C-600T-700 SERIES-750.
ASTRO-102BX-103.CYGNET-270B-300B.

## SHURE.

Shure- 444 schematic.

Shure- 522 schematic.

Shure- 527B schematic.

Shure- 550L schematic.


MORE SHURE MICROPHONE INFO.

## TEN TEC.

ORION / ARGONAUT / JUPITER.info and Schematic. 


TEN-TEC ORION - ARGONAUT - JUPITER - OMNI VI - PARAGON - DELTA II - CORSAIR - SCOUT-555
4 PIN PLUG.

PIN1        MIC +

PIN2        MIC -

PIN3        PTT

PIN4        +9 VOLTS.

SHELL/CHASSIS=GROUND

TEN-TEC ORION II / OMNI VII.
8 PIN PLUG.

PIN1        N/C

PIN2        +10 VOLTS

PIN3        N/C

PIN4        N/C

PIN5        GROUND

PIN6        PTT

PIN7        MIC EARTH

PIN8        MIC

OMNI-VII microphone info and Schematic.

ORION-II microphone info and Schematic.

TEN-TEC 705 MICROPHONE pdf

## TURNER.

TURNER- EXPANDER 500.schematic.

TURNER- EXPANDER 500 AMPLIFIER .schematic.

TURNER- M+2U - JM+2U.schematic.

TURNER- +3 AMPLIFIER.schematic.pdf

TURNER- SUPER SIDEKICK and +3 schematic.

TURNER- ROAD KING 56.schematic.

TURNER- RK60 / RK60J / PLUS+2 / M+3.schematic.

## VIKING.(E.F.Johnson Co)

VIKING-II.



VIKING RANGER -RANGER II -VALIANT -VALIANT II -VIKING 500 -INVADER 2000 -VIKING PACEMAKER -INVADER .

Pin 1 MIC.

Pin 2 PTT.

PLUG CASE EARTH.

VIKING MESSENGER.
40-50-80-4170-4175
VIKING.230-260-270-430.

Pin 1 MIC.

Pin 2 PTT/COMMON GROUND.

Pin 3 RECEIVE.

Pin 4 N/C.

Pin 5 PTT.

Pin 6 MIC SHIELD.

VIKING MESSENGER.
124

Pin 1 MIC.

Pin 2 PTT/COMON GROUND.

Pin 3 PTT.

Pin 4 N/C.

VIKING MESSENGER.
130-130A-132

Pin 1 MIC.

Pin 2 N/C.

Pin 3 PTT GROUND.

Pin 4 MIC GROUND.

Pin 5 SHIELD /MIC GROUND.

VIKING MESSENGER.
250

Pin 1 MIC.

Pin 2 PTT/COMON GROUND.

Pin 3 RECEIVE.

Pin 4 N/C.

Pin 5 PTT.

CASE SHIELD.

VIKING MESSENGER.
4230

Pin 1 PTT.

Pin 2 N/C.

Pin 3 PTT.

Pin 4 MIC.

Pin 5 N/C.

CASE SHIELD/COMMON GROUND.

VIKING MESSENGER.
4250

Pin 1 N/C

Pin 2 MIC.

Pin 3 PTT.

Pin 4 PPT/COMON GROUND.

Pin 5 N/C.

Pin 6 MIC SHIELD.

VIKING MESSENGER.
4730

Pin 1 PTT.

Pin 2 PTT.

CASE SHIELD/COMMON GROUND.

VIKING MESSENGER.
4740
VIKING 352-352D.

PIN 1 MIC.

PIN 2 PTT.

PIN 3 N/C.

PIN 4 N/C.

PIN 5 PTT/GROUND.

CASE SHIELD MIC GROUND.

VIKING MOBILE.